## Slide 1: Avoiding Information Leakage in the Memory Controller with Fixed Service Policies
The University of Texas at Austin
The University of Texas at Austin
Ali Shafiee, A. Gundu, M. Shevgoor, R. Balasubramonian and M. Tiwari

## Slide 2: Shared Memory Controller
Core1
$
MC
Core0
$
Chart: x10K Instructions
| 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0 | 110.0 | 120.0 | 130.0 | 140.0 | 150.0 | 160.0 | 170.0 | 180.0 | 190.0 | 200.0
low-traffic | 0 | 333333.333 | 666666.666 | 999999.999 | 1333333.332 | 1666666.665 | 1999999.998 | 2333333.331 | 2666666.664 | 2999999.997 | 3333333.33 | 3666666.663 | 3999999.996 | 4333333.329 | 4666666.662 | 4999999.995 | 5333333.328 | 5666666.661 | 5999999.994 | 6333333.327 | 6666666.66
high-traffic | 0 | 416666.667 | 833333.334 | 1250000.001 | 1666666.668 | 2083333.335 | 2500000.002 | 2916666.669 | 3333333.336 | 3750000.003 | 4166666.67 | 4583333.337 | 5000000.004 | 5416666.671 | 5833333.338 | 6250000.005 | 6666666.672 | 7083333.339 | 7500000.006 | 7916666.673 | 8333333.34

## Slide 3
Core 0
$
MC
3rd party
software
Core 1
$
Core 0: load changed
Core 1: access latency changed

## Slide 4: Fixed Service
RD
DM
WR
DM
WR
RD
time
Slot L
Quantum Q= 4xL
Goal: Minimize L
Such that
L is enough to transfer one read or one write
While
Satisfying cmd-to-cmd min time gaps
Data Placement relaxes time gaps
smart data placement  shorter L
0
1
2
3
CPU
Notes: Animated to make font bigger

## Slide 5: Mechanics of Memory
Data
Bus
CA
Bus
Rank 0
Rank 1
Bank
Bank
Bank
Bank
Memory Access
= ACT+ CAS
ACT
CAS

## Slide 6: Memory Constraints
 | ACT | CAS
ACT | 0 | 0
CAS | 0 | 6
Rank(A)  Rank(B)
 | ACT | CAS
ACT | 5 | 0
CAS | 0 | 4
Rank(0) Rank(0)
Bank(A)  Bank(B)
 | ACT | CAS
ACT | 5 | 11
CAS | 28 | 4
Rank(0) Rank(0)
Bank(A)  Bank(A)
1
2
1
2
1
2
tBURST
tRTRS
tBURST
tRRD
tFAW
tCCD tRCD
tRAS tRC
tRP tRTP

## Slide 7: Memory Partitioning
Rank-Part: Rank Partitioning
Bank-Part: Bank Partitioning
No-Part: No Partitioning
Core 0
Core 1
Core 2
Core 0
Core 1
Core 2
Core 3

## Slide 8: Formulating The Problem
RD
RD
WR
RD
RD
WR
time
Data Bus
0L
1L
2L
3L
4L
5L
time
CA Bus
ACT
CAS
TRCD
TCAS
CAS
ACT
TRCD
TCWD
KL-TCAS
KL-(TCAS+TRCD)
KL-TCWD
KL-(TCWD+TRCD)
Fixed Periodic
Transfer

## Slide 9: Rank Partitioning
Enough Time to Transfer
No Collision on CA Bus
L ≥TBURST+TRTRS  L ≥ 6
CAS(RD) ≠ CAS (WR)
KL-11 ≠ K’L-5
Rank-Part L=7
Bank-Part L=15
No-Part L=43
(K-K’)L ≠6  L≠6

## Slide 10: Bank-Part with Re-ordering
R
W
R
R
W
R
W
W
L=15
R
W
R
R
W
R
W
W
L=6
L=15
Return to CPU
en masse
Q=120
Q=63

## Slide 11: No-Part with Triple-Alternation
0
1
2
3
4
5
6
7
L=43
Q=344
0
1
2
3
4
6
6
7
L=15
0
1
2
3
4
5
6
7
Q=120
0
Memory
Bank
Bank
Bank
=
+
+
3x15=45>43
CPU
0
3
6
1
4
7
2
5
=

## Slide 12: Methodology
Simics
  8 4-way superscalar cores
  L1I (32K)/L1D (32KB)/L2 (1MB)  per core
USIMM
  1channel, 8 ranks, 8 banks
Benchmark
  SPEC 2006
  NPB
Compared with Temporal Partitioning (HPCA’14)

## Slide 13: Results
Increase OS complexity
RANK PARTITIONING
NO PARTITIONING
BANK PARTITIONING
PERFORMANCE
NON-SECURE
BASELINE
1.0
0.74
0.48
0.43
0.20
0.40
FS
FS: RD/WR-REORDER
FS: TRIPLE ALTERNATION
TP
TP
100%
12%
72%

## Slide 14: Conclusion
Shared MC  time-channel attacks
Fixed Service Policy
  Mathematical framework to reason about performance and security
  Rank-Part: L=7
  BP: L=15  Re-ordering L=6
  NP: L=43  Triple Alternation L=15
72% improvement over prior work (TP)

## Slide 15: Thank You 