## Slide 1: IMP: Indirect Memory Prefetcher
Xiangyao Yu1, Christopher J. Hughes2, Nadathur Satish2, Srinivas Devadas1
CSAIL, MIT1
Parallel Computing Lab, Intel2

## Slide 2: Sparse Operations
Operations on sparse datasets (e.g., graphs, sparse matrices) increasingly important
Reason #1: Rise of Big Data analytics
  Many analytics problems inherently irregular, represented by graphs or sparse systems of equations
Reason #2: HPC – big gains in dense apps have drawn attention to lousy efficiency of sparse apps
  Ex: High-Performance Conjugate Gradient (HPCG) in TOP500
  ALU utilization: DGEMM ~90%, SPMV ~1%-5%

## Slide 3: Challenge from Sparsity
Indirect access pattern
Example: sparse matrix-vector multiplication (SPMV)
Access pattern depends on input data
Traditional hardware prefetchers can not capture the pattern
×
matrix
non-zeros
input vector

## Slide 4: Execution Time Impact
62% execution time waiting for indirect accesses
Chart: Execution Time vs. Perfect Prefetch
| pagerank | tri_cnt | graph500 | sgd | lsh | spmv | symgs | avg
Indirect | 2.0388 | 2.2215 | 2.3977 | 0 | 0.26762 | 1.8329 | 1.1961 | 1.4221
Other | 0.4409 | 0.78406 | 0.56425 | 1.0136 | 1.5174 | 0.4719 | 1.3114 | 0.87192

## Slide 5: Observation
Indirect accesses generally in form of A[B[i]]
  Sparse matrix-dense vector multiplication
  A: input vector, B: column id of non-zeros
  Graph algorithms
  A: vertex list, B: edge list
B is pre-computed and contiguously accessed
Unpredictable factor is the content of B
  indirect_address = &A[B[i]] = coeff × B[i] + base_address
Key Idea: Indirect prefetch
On access to B[i] read B[i + Δ] and prefetch A[B[i + Δ]]
B
A

## Slide 6: IMP Architecture
Prefetch Table (PT)
Cache
Access
Address Generator
Indirect Prefetch
Address
Indirect prefetching
  &A[B[i]] = coeff × B[i + Δ] + base_address
Stream Table
Indirect Table

## Slide 7: IMP Architecture
Prefetch Table (PT)
Cache
Access
Address Generator
Indirect Prefetch
Address
Stream Table
Indirect Table
Indirect Pattern Detector (IPD)
Cache
Miss
Detect Indirect pattern
for stream accesses
Write detected indirect pattern
back to the prefetch table
Indirect pattern detection
  Learn coeff and base_address for A[B[i]]

## Slide 8: Indirect Pattern Detection
Need two (&A[B[i]], B[i]) pairs to solve for coeff and base_address
Candidates for &A[B[i]]: first several cache misses after accessing B[i]
  tend to do indirect access soon after reading index
  do not need to prefetch for cache hits
Restrict coeff to small powers of 2
  4, 8, 16, 1/8 (bit vector)
  Multiply becomes a shift
  Small set of values allows exhaustive search
  &A[B[i]] = coeff × B[i] + base_address

## Slide 9: Indirect Pattern Detector (IPD)
Events
Read idx1 (=1)
Miss addr=0x100
Miss addr=0x120
Read idx2 (=16)
Miss addr=0x13C
Ptr to Stream PF
index1
index2
Baseaddr array
Entry “X”
1
16
0xFC
0x11C
0xF8
0x118
0xF0
0x110
0x100
0x120
0xFC
0xBC
0x3C
0x13A
4
8
16
1/8
coeff
Given B[i] and B[i+1], for every following miss, compute base_address for every coeff
Match found! Coeff=4, base addr=0xFC
  &A[B[i]] = coeff × B[i] + base_address

## Slide 10: Other Optimizations
Multi-way indirection
  A[B[i]] and C[B[i]]
Multi-level indirection
  A[B[C[i]]]
Load partial cacheline for indirect accesses
  Little spatial locality
  IMP can help predict access granularity
See paper for details

## Slide 11: Evaluation
Graphite simulator
System configuration
  Core : 64 In-order, single issue
  L1 Cache: 32KB Dcache, 16KB Icache
  Shared L2 Cache: each tile 256 KB (16 MB in total)
  Memory: DRAMSim2
  On-die network: mesh, 2 cycles/hop, 64-bit flits
IMP configuration
  Prefetch table: 16 entries, max prefetch distance = 16
    storage overhead: less than 256 bytes
    energy overhead: less than 3%
  Indirect pattern detector: 4 entries
    storage overhead: 450 bytes

## Slide 12: Performance vs. Perfect Prefetcher
IMP gives 1.56x speedup on average
SW prefetch incurs 29% (up to 2x) more instructions
Chart: Speed up vs. Perfect Prefetch
| pagerank | tri_cnt | graph500 | sgd | lsh | spmv | symgs | avg
Baseline | 0.40328 | 0.33272 | 0.33761 | 0.98654 | 0.56023 | 0.43387 | 0.39881 | 0.4933
IMP | 0.94639 | 0.50781 | 0.70753 | 0.98769 | 0.69389 | 0.91899 | 0.63167 | 0.77057
SW Prefetch | 0.768 | 0.47041 | 0.66552 | 0.98777 | 0.60834 | 0.66027 | 0.56763 | 0.67542

## Slide 13: Summary
Indirect access (A[B[i]]) key pattern for workloads operating on sparse data structures
IMP can detect and prefetch these accesses at low hardware cost
Provides significant performance benefits

## Slide 14: Backup Slides

## Slide 15: Partial Cacheline Accessing
Chart: Speed up vs. Perfect Prefetch
| pagerank | tri_cnt | graph500 | sgd | lsh | spmv | symgs | avg
Baseline | 0.42273 | 0.33381 | 0.55707 | 0.97118 | 0.52736 | 0.43839 | 0.44647 | 0.52814
IMP | 1.0085 | 0.53089 | 0.68384 | 0.98948 | 0.65476 | 1.0047 | 0.71468 | 0.79811
IMP + Partial | 1.4783 | 0.62942 | 0.59683 | 0.98974 | 0.6204 | 1.0529 | 0.74223 | 0.87283

## Slide 16: Coverage
Chart: 
| pagerank | tri_cnt | graph500 | sgd | lsh | spmv | symgs | avg
Stream | 0.08 | 0.07 | 0.28 | 0.56 | 0.22 | 0.38 | 0.37 | 0.28
Stream + IMP | 0.96 | 0.91 | 0.74 | 0.67 | 0.78 | 0.99 | 0.87 | 0.85

## Slide 17: Accuracy
Chart: 
| pagerank | tri_cnt | graph500 | sgd | lsh | spmv | symgs | avg
Stream | 1 | 0.5 | 0.87 | 0.7 | 0.5 | 0.98 | 0.97 | 0.79
Stream + IMP | 1 | 0.72 | 0.94 | 0.72 | 0.66 | 0.98 | 0.96 | 0.85

## Slide 18: Latency vs. Perfect Prefetch
Chart: 
| pagerank | tri_cnt | graph500 | sgd | lsh | spmv | symgs | avg
Stream | 3.07 | 5.78 | 3.36 | 2.21 | 5.9 | 1.89 | 3.25 | 3.64
Stream + IMP | 1.13 | 3.57 | 1.16 | 1.68 | 4.04 | 1 | 2.01 | 2.15