## Slide 1: The CRISP Performance Model for Dynamic Voltage and Frequency Scaling in a GPGPU
Rajib Nath, Dean Tullsen
Micro 2015

## Slide 2: Dynamic Voltage & Frequency Scaling
DVFS
Power
Energy
Temperature
Reliability
Variability
Performance
Power
Energy
Temperature
Reliability
Variability
Performance
What is the performance impact of DVFS?

## Slide 3: DVFS Performance Model for GPGPUs
DVFS Opportunities in GPGPU
  GPGPU chips consume more power than CPU chips
  Provision for DVFS
  Voltage range is high
  Recent research shows energy saving opportunities
Challenges
  SIMD
  SIMT

## Slide 4
DVFS Performance Models for CPUs
Limitation of Existing Models
Critical Stalled Path (CRISP)
  Model Component
  Model Parameterization
  Hardware mechanism and overhead
Experiment
  Execution Time Prediction
  Energy Savings
Outline
DVFS Performance Models for CPUs
Limitation of Existing Models
Critical Stalled Path (CRISP)
  Model Component
  Model Parameterization
  Hardware mechanism and overhead
Experiment
  Execution Time Prediction
  Energy Savings

## Slide 5: DVFS Performance Model for CPUs
Proportionate
Sampling
Empirical
Analytical
β estimated from aggregate
metrics e.g., LLC miss counts
Does not account for MLP
Proportionate
Sampling
Empirical
Analytical
×1
×2

## Slide 6: Existing Analytical Models for CPUs
Stall counter [CF 2010]
Miss model [CF 2010]
Leading loads [TOC 2010]
Critical path [Micro 2012]
Fundamental Assumption
  Tmemory doesn’t scale with core frequency
  Cores never stall for stores
Accurate
Complex

## Slide 7
Outline
DVFS Performance Models for CPUs
Limitation of Existing Models
Critical Stalled Path (CRISP)
  Model Component
  Model Parameterization
  Hardware mechanism and overhead
Experiment
  Execution Time Prediction
  Energy Savings

## Slide 8
L1 Cache Miss
Memory/Computation Overlap
Store Stalls
Complex Stall Classification
L1 Cache Miss
Memory/Computation Overlap
Store Stalls
Complex Stall Classification
Fundamental Assumption of CPU based model
  Tmemory doesn’t scale with core frequency
  Cores never stall for stores
Limitation of CPU Models on GPGPUs
Challenges in GPGPU
SIMD & SIMT

## Slide 9: Limitation of CPU Models on GPGPUs
L1 Cache Miss
Memory/Computation Overlap
Store Stalls
Complex Stall Classification
Overlapped computations may make the kernel fully compute bound at a lower frequency
At frequency f
At frequency
At frequency

## Slide 10: Limitation of CPU Models on GPGPUs
L1 Cache Miss
Memory/Computation Overlap
Store Stalls
Complex Stall Classification
Ignoring the scaling of overlapped computation causes under prediction of execution time
At frequency f
At frequency

## Slide 11: Limitation of CPU Models on GPGPUs
Ignoring the scaling of overlapped computation causes under prediction of execution time
L1 Cache Miss
Memory/Computation Overlap
Store Stalls
Complex Stall Classification
Performance prediction
15 Core 48 Warp/Core
transition from memory bound to compute bound
frequency is reduced from left to right
prediction baseline frequency is 700 MHz

## Slide 12: Limitation of CPU Models on GPGPUs
L1 Cache Miss
Memory/Computation Overlap
Store Stalls
Complex Stall Classification
1 Core 1 Warp(32 Thread)
1 Core 1 Thread
Performance prediction
Settings | LSQ Full (Cycle%)
1 Core 1 Thread | 0
1 Core 1 Warp | 66
Ignoring store stall cycles causes over prediction of execution time
1 SIMD store may fork into 32 stores
transition from memory bound to compute bound
frequency is reduced from left to right
prediction baseline frequency is 700 MHz

## Slide 13
Outline
DVFS Performance Models for CPUs
Limitation of Existing Models
Critical Stalled Path (CRISP)
  Model Component
  Model Parameterization
  Hardware mechanism and overhead
Experiment
  Execution Time Prediction
  Energy Savings

## Slide 14: CRItical Stalled Path (CRISP)
GPGPU kernel has 3 different phases
  load outstanding, pure compute, store stall
Execution time= Load critical path + compute store path
Both LCP and CSP scale independently with frequency

## Slide 15: Load Critical Path (LCP) Portion
LCP is the longest sequence of dependent load latency [CRIT]
An LCP cycle is an overlapped computation or load stall
Overlapped computation
Load Stall
Load critical path
A=8
B=5
D=5
A=8
C=12
Dependent Loads
A  B
A  C
A  D
B  D

## Slide 16: Load Critical Path (LCP) Portion
lm – kernel
Overlapped computation
Load Stall
Load critical path
Prediction of
LEAD or CRIT
3
1
load
2
2
load
4
load
5
load
Compute store path
Frequency Scaling
transition
memory bound to compute bound
frequency is reduced from left to right

## Slide 17: Compute Store Path (CSP) Portion
Cycles outside LCP belongs to CSP
All the pure compute and store stall phases belongs to CSP
Non-overlapped
computation
Store Stall
Compute store path
`
Load critical path

## Slide 18: Compute Store Path (CSP) Portion
Non-overlapped computation
Store Stall
Compute store path
3
1
2
2
4
5
cfd – kernel
Frequency Scaling
transition
Memory bound  Compute bound
frequency is reduced from left to right

## Slide 19: CRISP Example
CRISP Components |  |  | 
LCP | 20 | CSP | 11
Load Stall | 3 | Store Stall | 1
Compute | 17 | Compute | 10
Model | Prediction (units 1/f) |  | 
 | TMemory | TCompute | Time (at f/2)
STALL | 4 | 27 | 58
MISS | 24 | 7 | 38
LEAD | 18 | 13 | 44
CRIT | 20 | 11 | 42
CRISP | 20 |  | 54
Existing Analytical Models
54 = max(17*2, 20) + max(11,10*2)
CRISP Model
31
54

## Slide 20: Hardware Mechanism & Overhead of CRISP
Hardware requirements
  3 counters: Global LCP, Load Stall, Store Stall
  One time stamp register (ts) per MSHR
20
Global LCP =
MSHR | ts | L | ts+L
 |  | 8 | 8
 |  | 5 | 13
 |  | 12 | 20
 |  | 5 | 18
Load Stall=
Store Stall=

## Slide 21: Hardware Mechanism & Overhead of CRISP
21
Global LCP = 21
MSHR | ts | L | ts+L
A | 0 | 8 | 8
B | 8 | 5 | 13
C | 8 | 12 | 20
D | 13 | 5 | 18
Load Stall= 4
Store Stall= 1
On load miss
  Update time stamp register (ts) with global LCP
On load stall
  Increment load stall counter and global LCP counter
On load returns after L
  Update global LCP with max(LCP, ts+L)
On store stall
  Increment store stall counter

## Slide 22
Outline
DVFS Performance Models for CPUs
Limitation of Existing Models
Critical Stalled Path (CRISP)
  Model Component
  Model Parameterization
  Hardware mechanism and overhead
Experiment
  Execution Time Prediction
  Energy Savings

## Slide 23: Execution Time Prediction
Reduces maximum error by 3.66 ×
Average prediction error 4% vs 11% with best alternative
Prediction error for all 6 target frequencies
Example prediction kernel – lm
Kernel makes transition between memory bound and compute bound at 300 MHz
frequency is reduced from left to right
prediction baseline frequency is 700 MHz

## Slide 24: Energy Savings
EDP optimum:
  EDP savings 10.72% vs. 6.72%
  Energy savings 12.87%
  Performance overhead 3.44%
ED2P optimum:
  ED2P 8.98% vs. 4.91%
lm- prediction
frequency is reduced from left to right

## Slide 25: Conclusion
Two fundamentals for performance models in GPGPUs
  Memory / computation overlaps
  Store related stalls
A runtime analytical model for DVFS in GPGPUs
  Better performance prediction accuracy
  Brings more energy savings
At frequency f
At frequency