## Slide 1: Cross-Architecture Performance Prediction (XAPP): Using CPU to predict GPU Performance
Newsha Ardalani
Clint Lestourgeon
Karthikeyan Sankaralingam
Xiaojin Zhu
University of Wisconsin-Madison

## Slide 2: Executive Summary
Problem: GPU programming is challenging
  Not clear how much speedup is achievable
Goal: Save programmers’ time from unnecessary porting effort
Insight:
  Speedup is correlated with program properties and hardware characteristics.
  Machine learning can learn the correlation
Results:
  27% relative error across 24 benchmarks

## Slide 3: Outline
Problem Statement
Insight
Overviews
Machine Learning Technique
Results
Future work

## Slide 4: Problem Statement
  For a given GPU platform, predict optimized GPU execution time obtainable for any CPU application prior to starting the code development process

## Slide 5: Insight
GPU performance GPU hardware characteristics
  Number of cores
GPU Performance Inherent program properties
  Available parallelism: Inherent program property
  Cache miss: platform-dependent program property
GPU Execution time =

## Slide 6: Overview
GPU Program
GPU Program
GPU Program
CPU Program
CPU Program
CPU Program
CPU Program
GPU Platformx
GPU Execution Time
…
…
Feature Vector
GPU Program
Training data
Machine Learning Model
Fx ( feature vector)
CPU Program
Predicted
GPU Execution Time
Dynamic Binary Instrumentation
Dynamic Binary Instrumentation

## Slide 7: Machine Learning Technique:
Prediction1
Prediction2
PredictionP
Training Set
n
m
Training Subset1
m
Training Subset2
m
Training Subsetp
…
…
Step-wise Regression
Step-wise Regression
Step-wise Regression
Majority Selection

## Slide 8: Outline
Problem Statement
Insight
Overviews
Machine Learning Technique
Results
Future work

## Slide 9: Results
Questions | Metrics | Results
How close is predicted speedup to actual speedup? | Accuracy | High
How robust across different GPU platforms? | Robustness | High
How much programmer involvement is required? | Usability | High
How quickly provide prediction? | Speed | High

## Slide 10: Experimental Setup
Accuracy results on GPU GTX 750
Training Set: 112 datapoints
  Rodinia, Lonestar, Parboil, Parsec Subset, NAS subset
Test Set: 24 datapoints
Feature Vector: 31 program properties
Program properties collected using MICA and Pin
Execution time measured on real GPU hardware

## Slide 11: Accuracy results
Chart: Speedup (CPU exec. time/ GPU exec. time)
| µ1 | µ5 | µ3 | particle_filter-rodinia | µ2 | µ4 | srad_v14-rodinia | b+tree2-rodinia | euler3d4-rodinia | ftv27-nass | b+tree1-rodinia | ftv26-nass | srad_v22-rodinia | sc1-rodinia | ftv24-nass | backprop2-rodinia | ftv20-nass | euler3d1-rodinia | bfs2-rodinia | euler3d2-rodinia | srad_v13-rodinia | nn1-rodinia | srad_v11-rodinia | srad_v15-rodinia
Measured | 0.8 | 1.1 | 1.3 | 1.4 | 1.8 | 1.9 | 3.7 | 4 | 4 | 4.1 | 4.5 | 6.2 | 6.2 | 6.4 | 6.6 | 10 | 10.4 | 10.6 | 13 | 23.3 | 34.4 | 39.7 | 108.8 | 109.2
Predicted | 1.5 | 1.3 | 1.6 | 1.8 | 2.5 | 3.4 | 3.5 | 4.5 | 1.5 | 6.8 | 5.5 | 8.4 | 8.3 | 4.8 | 5.6 | 9 | 24.6 | 8.8 | 9.2 | 10 | 15.7 | 32.3 | 77.3 | 108.8
Accuracy on platform 1 (GTX 750): 27% relative error
Accuracy on platform 2 (GTX 660): 36% relative error

## Slide 12: How to use our tool? Model Construction Phase
GPU Program
GPU Program
CPU Program
CPU Program
CPU Program
GPU Platformx
GPU Execution Time
…
…
Feature Vector
GPU Program
Training data
Machine Learning Model
Fx ( feature vector)
Provided

## Slide 13: How to use our tool? Usage Phase
CPU Program
STOP
START
Dynamic Binary Instrumentation
Fx ( feature vector)
Speedup Prediction

## Slide 14: One-time Cost Overhead
GPU Program
GPU Program
GPU Program
CPU Program
CPU Program
CPU Program
CPU Program
Dynamic Binary Instrumentation
GPU Platformx
GPU Execution Time
…
…
Feature Vector
GPU Program
Training data
Machine Learning Model
Fx ( feature vector)
0 min
30 min
~ 2.5 hr

## Slide 15: Recurring Overhead
GPU Program
GPU Program
GPU Program
CPU Program
CPU Program
CPU Program
CPU Program
Dynamic Binary Instrumentation
GPU Platformx
GPU Execution Time
…
…
Feature Vector
GPU Program
Training data
Machine Learning Model
Fx ( feature vector)
CPU Program
Dynamic Binary Instrumentation
Predicted
GPU Execution Time
~ 1 ms

## Slide 16: What it is not?
GPU Program
GPU Program
CPU Program
CPU Program
CPU Program
GPU Platformx
…
…
GPU Program
Training data
Machine Learning Model
Fx ( feature vector)

## Slide 17: Also in the paper
Why Ensemble Prediction?
Model Interpretation
End-to-End Case Studies

## Slide 18: Summary
CPU
GPU
CPU
GPU
FPGA
XeonPHI

## Slide 19: Questions?