## Slide 1: H3VP: History Based Highly Reliable Hybrid Value Predictor
Kenichi Koizumi, Kei Hiraki, Mary Inaba
The University of Tokyo

## Slide 2: Value Prediction (1/3)
Predict result values of executing instruction
Comparison to Branch Prediction
  Branch Prediction
    Single bit prediction (taken or not-taken)
    Speed-up by solving control dependencies
    Small penalty when prediction fails
  Value Prediction
    Multi-bit (32 or 64) prediction
    Speed-up by solving data-dependencies
    Large penalty when prediction fails

## Slide 3: Value Prediction (2/3)
Most branch predictors are history-based
  Simple predictors (e.g. last two values) have high hit-ratio.
  SOTA predictor shows very high hit-ratio.
Value prediction is much difficult
  Locality of result values exists but far less than that of branch
  About 50% executed instructions output last values and
  80% instructions output one of 16 latest results [Lipasti+,96]
  Much lower hit-ratio than branch predictors

## Slide 4: Value Prediction (3/3)
Miss penalty
  Latency of normal instruction < branch instruction
  Number of canceled instruction is much larger than that in branch prediction
Branch prediction
Value prediction
<<

## Slide 5: Existing studies
History-based prediction
  Last value [Gab96, LWS96] result of the last execution
  Reuse of Register value [TuSe99] target register
  Stride 2-delta [Gab96] Arithmetic sequence
  Last four value [BuZo99b, LiSh96]
Context-based prediction
  Finite context method [SaSm97a, SaSm97b]
    History length = 4, Exor indexed hashing
Confidence counter
  Selection for actual value prediction that are confident
    Selective Value Prediction[ CaReTu99]

## Slide 6: Our submission to CVP-1
We implemented three functions necessary to predict values and trigger speculation
All values are 64-bit.
  Some vector instructions split 128-bit into 64 bits.
We submitted all the three tracks:
    8kB, 32kB, Unlimited

## Slide 7: Inside the simulator(1/3)
getPrediction() is used to trigger speculation
  Successful speculation decreases the number of cycles
  Unsuccessful speculation increases the number of cycles
After triggering speculation, speculativeUpdate() shows the outcome of speculation
ID
EX
WB
getPrediction()
speculativeUpdate()
updatePredictor()
Seq#,PC
Trigger
Predicted value
Seq#,PC,speculation flag
Speculation result,type of the instruction , register values before execution
Seq#,Actual result value
Three functions necessary for simulation
IF
Instruction pipeline

## Slide 8: Inside the simulator(2/3)
updatePredictor() shows the correct result.
speculativeUpdate() shows register values (SRC, DST) before Execution.
  Register predictor in existing works uses only DST register
We cannot know detailed information other than Seq# and PC by getPrediction()
  Necessary value histories are stoted in tables. They can be accessed by
  (Seq#, PC).
ID
EX
WB
getPrediction()
speculativeUpdate()
updatePredictor()
Seq#,PC
Trigger
Predicted value
Seq#,PC,speculation flag
Speculation result,type of the instruction , register values before execution
Seq#,Actual result value
IF
Instruction pipeline

## Slide 9: Inside the simulator(3/3)
ID
EX
WB
IF
16 instruction fetch in a cycle
A number of getPrediction() and speculativeUpdate() are at first called without corresponding updatePredictor()
  That means these three functions are not atomic.
getPrediction()
speculativeUpdate()
updatePredictor()
getPrediction()
getPrediction()
speculativeUpdate()
speculativeUpdate()
16
ID
EX
WB
IF
ID
EX
WB
IF
ID
EX
WB
IF
16
ID
EX
WB
IF
ID
EX
WB
IF
ID
EX
WB
IF
16
ID
EX
WB
IF
ID
EX
WB
IF

## Slide 10: Observation of given traces(1/6)
90 % are ALU inst.
Remaining 10% are mostly memory loads
Instructio type | Prediction non-eligible | Prediction eligible | total
0 alu | 21013 | 476609 | 497622
1 load | 0 | 62695 | 62695
2 store | 218396 | 2870 | 221266
3 condBranch | 227459 | 0 | 227459
4 uncondDirectBranch | 3137 | 3164 | 6301
5 uncondIndirectBranch | 4589 | 58 | 4647
6 fp | 0 | 18 | 18
7 slowAlu | 0 | 846 | 846
total | 474594 | 546260 | 1020854
Contents of 1M trace of CVP-1

## Slide 11: Observation of given traces(2/6)
Half of PCs show Periodicity
  Period of most periodic instructions is 1 (i.e. Constant)
Period | # of PCs | # of Inst
1 | 895 | 41515
2 | 26 | 1652
3 | 17 | 702
4 | 6 | 256
5--8 | 26 | 1453
None | 840 | 499898
Total | 1810 | 545476
1M trace
Our predictor

## Slide 12: Observation of given traces(4/6)
CDF(cumulative distribution function) of actual values on 1M trace
  Values more than 33 bits rarely become actual value to be predicted
32bit:98.7%
27bit:51.7%
26bit:29.5%
19bit:25.7%
Bit width
CDF

## Slide 13: Observation of given traces(5/6)
13 traces are FP computations.
  Distribution of values in compute_fp_4(first 1M instructions)
    About 30～35% use 64 bit data
32bit:64.9%
25bit:35.9%
Bit width

## Slide 14: Observation of given traces(6/6)
Large penalties on misprediction
    Exact costs are unknown
    Our estimation
      80～100 hit ≒ 1 miss

## Slide 15: Our strategies – (1)History-based Prediction
Forget PC without periodicity
    Even when we use complicated predictor, learned by 30 execution history and it predict correctly 70 times, only one failure cancels all the benefit of complicated prediction.
We ignore long lengthy periodicity
    The amount of memory is proportional to the max length of periodicity
We choose the length of period to 1, 2 and 3.
  1 : Constant generation, loading constant
  2 : Tuple data etc.
  3 : 3D space computation

## Slide 16: Our Strategies – (2)Hybrid Predictors
Predict for periodic sequences
  Combine 2-peridoc predictor and 3-periodic predictor
  Period 1(Constant value) can be predicted using 2-periodic and 3-periodic predicters
Predict for arithmetic sequences
  Arithmetic sequence is easy to predict and use small amount of memory
When one of three predictor detects effective prediction, speculation is triggered.
Three predicters share History table to reduce memory use
Speculation
command integrator
Execution
information
(1) Arithmetic predictor
(2) Two-periodic predictor
(3) Three-periodic predictor
Speculation
command
History
table

## Slide 17: Our Strategies – (3) High Reliability
To avoid speculation failures
  Wait until confidence counter reaches the specified threshold
Use Two-step confidence threshold
  A small threshold is used as long as no prediction miss occurs
  A large threashold is used after the first misprediction
Effective use of storage
  When another PC assigned to the already used hash entry is executed three successive times, entry assignment is updated

## Slide 18: Periodicity Coverage of Our Predictor
Static periodicity
    Periodicity determined statically by algorithm
    Loop structure with fixed number of iterations
  Dynamic periodicity
    Periodicity determined dynamically by control flow of the program
    Loop structure with variable number of iterations
Static periodicity | Dynamic periodicity | Coverage | Reason
Short(~3) | Short(~100) | × | Below 2nd conf. threshold Miss penalty is larger than benefit Forget speculation
Short(~3) | Long(100~) | 〇 | Our Target of speculation
Long(4~) | Any | × | Predictable by simple predictor Bad cost/performance Forget speculation
None | Any | × | Impossible by light-weight predictor Forget spaculation

## Slide 19: State Machine for Speculation (1/3)
Correct & over threshold
Miss
Different PC
Different PC
Different PC
Same PC
Same PC
INIT
PREPARE
VERIFY
SPECULATE
Correct
Correct &
under threshold
FAILED
New PC
Different PC
Miss

## Slide 20: State Machine for Speculation (2/3)
INIT
  No instruction execution information has been provided
  The entry has not been assigned to any PC
PREPARE
  The entry has yet to obtain sufficient information to determine regularity
VERIFY
  The entry has obtained sufficient information
  Prediction reliability has not reached the threshold

## Slide 21: State Machine for Speculation (3/3)
SPECULATE
  Prediction reliability has reached the threshold
  Speculating
FAILED
  Misprediction has occurred
Change assigned PC
  A PC that is different from the currently assigned PC is executed three times in succession
  Discard the information about the currently assigned PC
  Assign the entry to the new PC

## Slide 22: H3VP Block Diagram (1/2)
Predict value of the next execution
E.g., arithmetic predictor outputs Hist0+Diff
If prediction is correct, counter will be incremented
PC
Hist0
Hist1
Hist2
Diff
hash( )
PC
Actual value
History table
Increment confidence counter
Calculate prediction value
PC is hashed to generate an index of history table
Hist0: value of the latest execution
Hist1: value of the previous execution
Hist2: value of the one preceding execution
Diff: Hist0 - Hist1

## Slide 23: H3VP Block Diagram (2/2)
If at least one of three confidence counters exceeds threshold, speculation becomes active
Regardless of whether speculation is active, status is set to FAILED if prediction misses
Status
Cnf
Status
Cnf
Status
Cnf
Confidence threshold
Speculate
Arithmetic
Status & confidence counter of Predictors
2-periodic
3-periodic

## Slide 24: Storage Budget
Storage consumption of single entry
 | Field | Bit width [bit]
History table | PC, Hist0, Hist1, Hist2, Diff, NewPC | 64 * 6 = 384
 | Counter for NewPC | 2
Predictor (* 3 predictors) | State machine | 3 * 3 = 9
 | Conf. counter | 8 * 3 = 24
 | Failed flag | 1 * 3 = 3
Total |  | 422

## Slide 25: Evaluation
135 traces of CVP-1
Geometric mean of IPC
Predictors for 8 kB 32 kB and Unlimited are exactly same
  We use different # of entries and 1st confidence threshold
Tracks | 8 kB | 32 kB | Unlimited
# of entries | 128 | 512 | 1048576
Storage | 6.59 kB | 26.4 kB | 52.8 MB
1st conf. thres. | 24 | 10 | 10
2nd conf. thres. | 112 | 112 | 112

## Slide 26: Overall Scores
No prediction (baseline): 3.211
H3VP (camera ready deadline)
  8 kB: 3.341 (+4.06%)
  32 kB: 3.378 (+5.19%)
  Unlimited: 3.582 (+11.56%)
Reference (H3VP in first submission deadline)
  8 kB: 3.226 (+0.47%)
  32 kB: 3.251 (+1.25%)
  Unlimited: 3.436 (+7.01%)

## Slide 27: Benchmark Results of Individual Predictors
High IPC is achieved by integrating Periodic predictors and Arithmetic predictor
Chart: Average IPC
| Constant | Arithmetic | 2-periodic | 3-periodic | H3VP
8 kB | 3.2248 | 3.3221 | 3.2261 | 3.2417 | 3.3412
32 kB | 3.254 | 3.3557 | 3.2562 | 3.2713 | 3.3775
Unlimited | 3.425 | 3.5292 | 3.456 | 3.445 | 3.5821

## Slide 28: Selection of Confidence Threshold (1/2)
Too Small
  We cannot avoid failure of speculation due to an appearance of an irregular value with a period length longer than the threshold value
Too Large
  the beginning of speculation delays and the predictor will miss out rewards for speculation success
Performance varies greatly depending on 2nd conf. threshold
Optimal threshold is determined by the ratio of the acceleration rewards on speculation success to the rewinding penalty on speculation failure

## Slide 29: Selection of Confidence Threshold (2/2)
Optimal value of 2nd conf. thres. is 112 in all tracks
Optimal value of 1st conf. thres.: 24 (8kB track), 10 (32kB and unlimited tracks)
Chart: The 2nd confidence threshold
| 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60 | 64 | 68 | 72 | 76 | 80 | 84 | 88 | 92 | 96 | 100 | 104 | 108 | 112 | 116 | 120 | 124 | 128 | 132 | 136 | 140 | 144 | 148 | 152 | 156 | 160 | 164 | 168 | 172 | 176 | 180
8 kB | 3.3294 | 3.3341 | 3.3358 | 3.3371 | 3.337 | 3.3392 | 3.3393 | 3.3393 | 3.339 | 3.3388 | 3.3397 | 3.3394 | 3.339 | 3.3386 | 3.3381 | 3.3377 | 3.3375 | 3.3373 | 3.3372 | 3.3392 | 3.3399 | 3.3399 | 3.3412 | 3.341 | 3.3408 | 3.3408 | 3.3406 | 3.3406 | 3.3403 | 3.3401 | 3.3399 | 3.3397 | 3.3395 | 3.3393 | 3.339 | 3.3388 | 3.3386 | 3.3383 | 3.3381 | 3.3379
32 kB | 3.3577 | 3.3635 | 3.3658 | 3.3677 | 3.3677 | 3.37 | 3.3703 | 3.3704 | 3.3703 | 3.3702 | 3.3736 | 3.3738 | 3.3734 | 3.3731 | 3.3727 | 3.3725 | 3.3723 | 3.3722 | 3.3721 | 3.3755 | 3.3762 | 3.3762 | 3.3775 | 3.3773 | 3.3771 | 3.3772 | 3.3771 | 3.3771 | 3.3768 | 3.3765 | 3.3764 | 3.3761 | 3.3759 | 3.3757 | 3.3754 | 3.3751 | 3.3749 | 3.3747 | 3.3744 | 3.3742
Chart: The 2nd confidence threshold
| 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60 | 64 | 68 | 72 | 76 | 80 | 84 | 88 | 92 | 96 | 100 | 104 | 108 | 112 | 116 | 120 | 124 | 128 | 132 | 136 | 140 | 144 | 148 | 152 | 156 | 160 | 164 | 168 | 172 | 176 | 180
Unlimited | 3.537 | 3.549 | 3.5585 | 3.5636 | 3.5661 | 3.5694 | 3.5708 | 3.5717 | 3.5721 | 3.5729 | 3.5772 | 3.5774 | 3.5772 | 3.577 | 3.5769 | 3.5765 | 3.5762 | 3.5762 | 3.5759 | 3.5803 | 3.581 | 3.5808 | 3.5821 | 3.5817 | 3.5815 | 3.5817 | 3.5815 | 3.5811 | 3.5804 | 3.5798 | 3.5793 | 3.5788 | 3.5783 | 3.5777 | 3.5771 | 3.5766 | 3.5761 | 3.5756 | 3.575 | 3.5746
112
112
112

## Slide 30: Benchmark Results of Individual Traces (1/2)
Chart: IPC improvements [%]
Chart: IPC improvements [%]
Chart: IPC improvements [%]
compute_int
compute_fp
srv
633%
147%
H3VP IPC improvements for 135 CVP-1 traces
8 kB
32 kB
Unlimited
633%
169%
633%
169%

## Slide 31: Benchmark Results of Individual Traces (2/2)
compute_fp shows low performance
    Arithmetic predictor in H3VP uses integer adder/subtractor and can predict integer arithmetic sequences
    Possibly arithmetic predictor using FP-adder/subtractor is effective

## Slide 32: Summary
H3VP: History Based Highly Reliable Hybrid Value Predictor
  Focus on speculation targets that can be characterized by arithmetic or periodic sequences
  Suppresses the increase in storage consumption, while maintaining large history table for wide coverage
IPC improvements on CVP-1
  +4.06% (8 kB), +5.19% (32 kB), +11.56% (Unlimited)