## Slide 1: Exploring Value Prediction with the EVES predictor
André Seznec
IRISA/INRIA

## Slide 2: Remove Data depencies with Value Prediction [Lipasti96][Mendelson97]
I1
I2
I3
I4
I5
t
ILP = 1
I1
I2
I3
I4
I5
ILP = 2
I6
I6
Predict result of I3
in advance
Validate prediction
when I3 executes

## Slide 3: Value Prediction
Large body of research 96-02
Quite efficient:
    Surprisingly high number of predictable results
    Sometimes up to 90 % !!
Not implemented so far:
Why ?

## Slide 4: The conventional (expert) wisdom on VP
Complexity/power at any pipeline stage:
    Untractable critical path for prediction
    Untractable repair on misprediction
    Huge extra complexity in the execution core
          Extra register file ports for prediction writes and validations
          Extra data paths for validations

## Slide 5: The conventional (expert) wisdom on VP
Complexity/power at any pipeline stage:
    Untractable critical path for prediction
    Untractable repair on misprediction
    Huge extra complexity in the execution core
          Extra register file ports for prediction writes and validations
          Extra data paths for validations
2013-2015
That’s not true !!

## Slide 6
What we showed:
  VTAGE predictor: high coverage, no critical path
  Validation/repair can be delayed till commit
  only use high confidence predictions
  EOLE: VP enables to simplify the OoO core

## Slide 7: Championship to promote VP ?
I was skeptical:
  Framework:
    Independence from the microarchitecture?
    Prediction validation?
  Which metric?
What can be learned?
But I add to compete and did learn 😇

## Slide 8: The value predictors
Two families of predictors:
Context based predictors:
  -predict a value already been seen in a similar context
    PC: last value predictor
    PC+ value history: FCM predictor
    PC + branch history: VTAGE
Computational predictors:
  -compute the value from previous occurrence
    The stride predictor
    + hybrid predictors D-FCM, D-VTAGE

## Slide 9: EVES: Enhanced VTAGE Enhanced Stride
Combines a context predictor and a computational predictor
  VTAGE based
  Stride based
Eliminate null strides:
  Address distinct instructions

## Slide 10: Conventional stride predictor
Prediction
Stride
Retired Last Value
Speculative Window
Prediction can be used only if it is high confidence
If any low confidence prediction occurrence in the pipeline: low confidence
High
High
Low
Low

## Slide 11: E-Stride predictor
Inflight
Val
Stride
Val + (Inflight+1) *Stride
Speculative
window
Val/Stride
table
Update at commit
PC
Confidence
Inflight = number of speculative occurrences of the instruction

## Slide 12: VTAGE: global branch history
VT0
pred
use
ghist[0,L(N)]
VT1
VTN
pred ctr
pred ctr tag
pred ctr tag
…
=?
=?
hash
hash
hash
hash
pc
pc
pc
ghist[0,L(1)]
The rightmost
matching component
Predicts
Sat?

## Slide 13: What VTAGE is Really About
Global history is non-speculative
The result of the previous instance is not required:
  No speculative window.
  No prediction critical loop
In our simulations (HPCA 2014),
more efficient than FCM predictors

## Slide 14: What is not that great with VTAGE
Tagless entries on the base predictor:
  Inherited from ITTAGE, but VP is different:
  Prediction is not mandatory
Wide entries: 64 bits + tag + confidence + replacement
  Most allocated entries never useful

## Slide 15: E-VTAGE
Tagged base predictor + associativity
Do not store the 64-bit values, but a hash or a pointer
Share the overall storage space among all logical tables

## Slide 16
Hit or miss
Values
Validity
Hash/pointer
confidence
tag
Increasing history length

## Slide 17
That’s all for the predictors layout !!
But most of the benefits come from:
  Confidence management
  Insertion/replacement

## Slide 18: All predictions are not equal !!
Better predicting a load missing the LLC than a simple ALU !
  need for less correct pred. to amortize a misp.
Better predicting a large value than a null (or small) value

## Slide 19: Update confidence on the E-stride predictor
Extensive use of probabilistic confidence counters
  5-bit
  High confidence if C>6
  Decrease by 4 on mispredictions
    restart predicting immediately after most misp
Increment probabilities by inst. types and latencies
  From 1 for a load LLC miss to for an ALU op
  And less if the stride is small

## Slide 20: Insert/Evict on the E-stride predictor
Favor high reward instructions
Evict useless entries
    Insert with probability 1 on a load LLC miss
    with probability on a ALU op
48 entries capture the overall potential
on the distributed traces

## Slide 21: Update confidence on E-VTAGE
Probabilistic confidence counters
  3-bit
  High confidence if C==7
  Decrease by 2 on misp. with C==7, reset otherwise
Increment probabilities by inst. types, latencies and values
  From 1 for a load LLC miss to for an ALU op
  Much less if the value is null or small

## Slide 22: Insert/Evict on E-VTAGE
Favor high reward instructions/value
Evict useless entries
Systematic allocation on a ”misprediction”
    (already medium confidence)
    On the 32KB predictor:
    Insert with probability 1 on a load LLC miss
    to probability on a ALU op with null result

## Slide 23
All the probabilities were defined
for the CVP framework
Should be adapted for effective designs:
  Fetch/Issue width
  Instruction window size
  Instruction latency
  Memory hierarchy

## Slide 24: Miscelleanous
To avoid slowdowns:
Safety nets to limit bursts of mispredictions

## Slide 25: Performance of E-Stride
48-entry, 106 bits per entry ➡ 5,088 bits
conventional stride: + 3.1 % 😖😖
+ confidence and insertion prob.: + 3.7 % 😖
+ E-Stride algorithm: +10.4 % 🤗😇
+ smart confidence reset : +16.1% 🤗😇🤠😎

## Slide 26: Performance Analysis of E-Stride
More than 10 % on 41 out of 135 traces
Up to 1090 %, more than 100 % on 12 traces
Very limited prediction coverage: 3.4 % (up to 56.7 %)
Not that high accuracy: 99.3 %
Predicting only loads: 15.8 % (1.3 % coverage)

## Slide 27: Performance of E-VTAGE
8KB ➡ 1,504 entries, 384 64-bit values
7.0 % performance increase
14.5 % prediction coverage
32KB ➡ 6,272 entries, 1,536 64-bit values
11.2 % performance increase
23 % prediction coverage

## Slide 28: Performance Analysis of 32KB E-VTAGE
More than 10 % on 40 out of 135 traces (up to 149 %)
Very high accuracy: 99.95 %
➡Less high reward predictions than E-Stride
Predicting only loads:
  10.4 %⬌11.2 % (17 % prediction coverage)
Last Value Predictor: 6.7 %

## Slide 29: Performance of EVES
32KB predictor
30.8% performance increase
More than 20 % on 54 out of 135 traces
Up to 1090 %, more than 100 % on 15 traces
8KB predictor
25.3% performance increase
More than 20 % on 50 out of 135 traces
Up to 1090 %, more than 100 % on 15 traces

## Slide 30: Performance Analysis of EVES
E-VTAGE and E-Stride do not predict the same instructions
Performance benefits are multiplicative
E-Stride is the most rewarding

## Slide 31: Unlimited EVES predictor
37.3 % performance increase
49 % prediction coverage
Could be augmented with other prediction schemes
  FCM, address prediction, D-FCM, D-VTAGE

## Slide 32: Conclusion
EVES combines 2 simple predictors:
  Limited access to speculative information
  No critical loop in prediction
Differentiated confidence updating is key for performance
High performance potential at limited storage budget
On a EOLE architecture with EVES,
40 % of the instructions would not enter the OoO core