## Slide 1: A Mostly-Clean DRAM Cache for Effective Hit Speculation and Self-Balancing Dispatch
Jaewoong Sim Gabriel H. Loh Hyesoon Kim
Mike O’Connor Mithuna Thottethodi

## Slide 2: A Mostly-Clean DRAM Cache for Effective Hit Speculation and Self-Balancing Dispatch
Problems: Inefficiencies on current DRAM cache approach
  Multi-MB/High-latency cache line tracking structure (MissMap)
  Under-utilized aggregate system bandwidth
Solutions: Use speculative techniques
  Replace MissMap with a low-cost Hit-Miss Predictor (HMP)
  Dynamically steer hit requests either to DRAM$ or off-chip DRAM (SBD)
  Maintain a mostly-clean DRAM cache via Dirty Region Tracker (DiRT)
Results: Make DRAM cache approach more practical
  20.3% faster than no DRAM cache (15.4% over the state-of-the-art)
  Removed 4MB storage requirement (employable in commercial products)
New Approach: Region-Based Prediction!
+ TAGE Predictor-like Structure!
= Less than 1KB Storage!!
New Approach: Hybrid Region-Based WT/WB policy for DRAM$!
Stacked
DRAM$
Off-chip
DRAM
Another Hit Request
Req. Buffer
Req. Buffer
Always send hit requests to DRAM$?
Off-chip BW is under-utilized!
3 tag blocks
29 data blocks
Row Decoder
Sense Amplifier
DRAM Bank
…
2KB DRAM ROW
MissMap
4MB size for 1GB DRAM$!! 
20+ cycles access latency!! 
Provide the cache line existence info (hit or miss)