## Slide 1
KnightShift: Scaling the Energy Proportionality Wall Through Server-Level Heterogeneity
Daniel Wong Murali Annavaram
University of Southern California
MICRO-2012
Supported by NSF and DARPA

## Slide 2: Overview
Overview | 2
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.95078 | 0.90415 | 0.84715 | 0.79275 | 0.74611 | 0.69689 | 0.65285 | 0.60363 | 0.53368 | 0.37565
Linear | 1 | 0.93756 | 0.87513 | 0.81269 | 0.75026 | 0.68782 | 0.62539 | 0.56295 | 0.50052 | 0.43808 | 0.37565
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
Chart: Time
Trend | 0.33811 | 0.37764 | 0.55402 | 0.64078 | 0.64683
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.95078 | 0.90415 | 0.84715 | 0.79275 | 0.74611 | 0.69689 | 0.65285 | 0.60363 | 0.53368 | 0.37565
Linear | 1 | 0.93756 | 0.87513 | 0.81269 | 0.75026 | 0.68782 | 0.62539 | 0.56295 | 0.50052 | 0.43808 | 0.37565
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
KnightShift | 1.0244 | 0.97513 | 0.9285 | 0.8715 | 0.8171 | 0.77047 | 0.72124 | 0.6772 | 0.064826 | 0.044589 | 0.024352
1. Measuring EP
2. EP Trends
3. KnightShift
4. Effect on EP
5. Evaluation

## Slide 3: Measuring Energy Proportionality
Measuring EP | 3
Energy Proportionality Curve
Actual – empirically measured power usage
Linear – extrapolated from peak to idle power usage
Ideal – utilization and power are perfectly proportional
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.95078 | 0.90415 | 0.84715 | 0.79275 | 0.74611 | 0.69689 | 0.65285 | 0.60363 | 0.53368 | 0.37565
Linear | 1 | 0.93756 | 0.87513 | 0.81269 | 0.75026 | 0.68782 | 0.62539 | 0.56295 | 0.50052 | 0.43808 | 0.37565
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
Server B
Server A
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.93713 | 0.85725 | 0.79737 | 0.73246 | 0.68054 | 0.64263 | 0.61072 | 0.5688 | 0.53988 | 0.5
Linear | 1 | 0.95 | 0.9 | 0.85 | 0.8 | 0.75 | 0.7 | 0.65 | 0.6 | 0.55 | 0.5
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0

## Slide 4: Dynamic Range (DR)
DR is a course first-order approximation of EP
  …but it is not accurate – only measures two extremes
  Ignores power consumption at intermediate utilizations
Assuming 100W peak and Google datacenter utilization[1]
  Server A = 68.6W , Server B = 64.6W
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.93713 | 0.85725 | 0.79737 | 0.73246 | 0.68054 | 0.64263 | 0.61072 | 0.5688 | 0.53988 | 0.5
Linear | 1 | 0.95 | 0.9 | 0.85 | 0.8 | 0.75 | 0.7 | 0.65 | 0.6 | 0.55 | 0.5
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.95078 | 0.90415 | 0.84715 | 0.79275 | 0.74611 | 0.69689 | 0.65285 | 0.60363 | 0.53368 | 0.37565
Linear | 1 | 0.93756 | 0.87513 | 0.81269 | 0.75026 | 0.68782 | 0.62539 | 0.56295 | 0.50052 | 0.43808 | 0.37565
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
Measuring EP | 4
DR=60%
DR=50%
[1] L. Barroso and U. Holzle,“The Case For Energy-proportional Computing,” Computer, Dec 2007.
How can we accurately quantify EP?

## Slide 5: Energy Proportionality (EP)[2]
EP is a better indicator of energy usage than DR
Why is DR not enough?
  EP = DR + how linear the energy proportionality curve
Measuring EP | 5
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.95078 | 0.90415 | 0.84715 | 0.79275 | 0.74611 | 0.69689 | 0.65285 | 0.60363 | 0.53368 | 0.37565
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
[2] F. Ryckbosch, S. Polfliet, and L. Eeckhout, “Trends in Server Energy Proportionality,” Computer,2011.
EP=53%
EP=57%
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.93713 | 0.85725 | 0.79737 | 0.73246 | 0.68054 | 0.64263 | 0.61072 | 0.5688 | 0.53988 | 0.5
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
???

## Slide 6: Linear Deviation (LD)
Linearly Energy Proportional (LD=0) EP=DR
Superlinearly Energy Proportional (+LD) EP<DR
Sublinearly Energy Proportional (-LD) EP>DR
LD shows how far off the actual EP curve is from the linear EP curve
Measuring EP | 6
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.95078 | 0.90415 | 0.84715 | 0.79275 | 0.74611 | 0.69689 | 0.65285 | 0.60363 | 0.53368 | 0.37565
Linear | 1 | 0.93756 | 0.87513 | 0.81269 | 0.75026 | 0.68782 | 0.62539 | 0.56295 | 0.50052 | 0.43808 | 0.37565
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
Superlinear
Sublinear
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.93713 | 0.85725 | 0.79737 | 0.73246 | 0.68054 | 0.64263 | 0.61072 | 0.5688 | 0.53988 | 0.5
Linear | 1 | 0.95 | 0.9 | 0.85 | 0.8 | 0.75 | 0.7 | 0.65 | 0.6 | 0.55 | 0.5
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0

## Slide 7: Proportionality Gap (PG)
Proportionality Gap (PG) @ utilization x%
Measuring EP | 7
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.95078 | 0.90415 | 0.84715 | 0.79275 | 0.74611 | 0.69689 | 0.65285 | 0.60363 | 0.53368 | 0.37565
Linear | 1 | 0.93756 | 0.87513 | 0.81269 | 0.75026 | 0.68782 | 0.62539 | 0.56295 | 0.50052 | 0.43808 | 0.37565
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.93713 | 0.85725 | 0.79737 | 0.73246 | 0.68054 | 0.64263 | 0.61072 | 0.5688 | 0.53988 | 0.5
Linear | 1 | 0.95 | 0.9 | 0.85 | 0.8 | 0.75 | 0.7 | 0.65 | 0.6 | 0.55 | 0.5
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
 | 0 | 0.037126 | 0.057246 | 0.097365 | 0.13246 | 0.18054 | 0.24263 | 0.31072 | 0.3688 | 0.43988 | 0.5
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
 | 0 | 0.050777 | 0.10415 | 0.14715 | 0.19275 | 0.24611 | 0.29689 | 0.35285 | 0.40363 | 0.43368 | 0.4

## Slide 8: Energy Proportionality Trends
SPECpower_ssj2008
  Measures performance and power at 10% utilization intervals
291 servers
November 2007 – December 2011
Trends | 8

## Slide 9: Dynamic Range Trends
2007-2009
  DR improves from 50% to 80%
Since 2009
  DR stalled at 80%
100% DR very difficult
  Power supplies, voltage converters, fans, chipsets, network, etc.
Trends | 9
Chart: Time
 | 0.37002 | 0.40217 | 0.42884 | 0.49687 | 0.62156 | 0.67248 | 0.69411 | 0.59734 | 0.69611 | 0.69611

## Slide 10: Energy Proportionality Trends
Chart: Time
 | 0.34631 | 0.36803 | 0.39353 | 0.47012 | 0.57702 | 0.63494 | 0.6436 | 0.58092 | 0.67218 | 0.67218
EP also stalled around 80%
  Caused by DR
High EP servers are -LD
Trends | 10
Since DR growth stalled, the only way to improve EP is through lowering LD

## Slide 11: Proportionality Gap Trends
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
LOW(<50) | 0 | 0.072204 | 0.13845 | 0.2013 | 0.26239 | 0.3202 | 0.37647 | 0.43274 | 0.48914 | 0.54259 | 0.59212
MID(50-75) | 0 | 0.032603 | 0.066184 | 0.099045 | 0.1345 | 0.17513 | 0.22064 | 0.26968 | 0.32188 | 0.36577 | 0.32569
HIGH(75+) | 0 | 0.018621 | 0.022392 | 0.027864 | 0.035904 | 0.062013 | 0.098872 | 0.14383 | 0.19641 | 0.2419 | 0.24113
Large PG at low utilization regardless of EP
As EP improves, PG at high utilization near 0
Trends | 11
Energy disproportionality at low utilization will be the main obstacle to achieving perfectly ideal EP

## Slide 12: Energy Efficiency Trends
Chart: Time
Energy efficiency is defined as ssj_ops/watt
Energy efficiency at high load has grown dramatically
Energy efficiency at low load has grown slowly
Most datacenter workloads spent majority of time at low load
Trends | 12
Low utilization energy efficiency growth must be addressed to improve overall server energy efficiency

## Slide 13: Overcoming the EP Wall
EP stall primarily caused by stall in DR
  Main focus has been improving peak and idle power consumption
To improve EP in the future:
  Improve LD
  Target large proportionality gap at low utilizations
Previous server-level low power modes are inactive
  Exploits idle periods  DR improvements
There is now a need for server-level active low power modes
  Exploits low utilization periods  LD/PG improvements
Trends | 13

## Slide 14: KnightShift Server Architecture
Server-level active low power mode solution to exploit low utilization periods
Basic Idea -- fronts a high-power primary server with a low-power compute node, called the Knight
Knight capability = fraction of throughput compared to primary server
KnightShift consists of 3 components:
  KnightShift hardware
  System software
    Supports certain functionality (data sharing, networking, etc)
  KnightShift runtime
    Supports KnightShift functionality
KnightShift | 14

## Slide 15: Ensemble-level KnightShift
Primary Server and Knight contains independent CPU/Memory/Chipset
Independent power domains
  Remote wakeup through wake-on-lan
Shared Disk (NFS)
Networking through simple router
  Communicate b/t both nodes
  Expose only Knight’s IP
  Requires Knight to stay on
Implementation Options:
  Ensemble-level (Commodity parts)
  Board-level (Motherboard Intg.)
  Server-level (Add-on board)
KnightShift | 15

## Slide 16: KnightShift Runtime
Example KnightShift operation
KnightShift | 16
Sleep
Wakeup
awake
sync
Low
High
 Power Consumption 
Primary: Flush
memory state
Primary: Send sleep message and enter low power state
Knight: Begin processing request
Knight: Sends wakeup message
Primary: Wakes up and sends awake message
Knight: Flush memory state. Sends sync message.
Primary: Begin processing requests
Primary Server
Knight

## Slide 17: KnightShift Runtime
Monitors server utilization
Mode switching policy
  Aggressively switch into the Knight
  Conservatively switch out off the Knight
  More optimized policy will improve response time at cost of energy
Redirect requests (Using scheduler/web balancer)
  Forward incoming requests to active node
Coordinating mode switching
  Ensure data consistency
KnightShift | 17

## Slide 18: Effect of KnightShift on EP
KnightShift-enhanced 291 SPECpower servers
Theoretically scale power of Knight
  PowerKnight = C1.7 × PowerPrimary, with Knight capability C
KnightShift EP | 18
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
Actual | 1 | 0.95078 | 0.90415 | 0.84715 | 0.79275 | 0.74611 | 0.69689 | 0.65285 | 0.60363 | 0.53368 | 0.37565
Ideal | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
KnightShift | 1.0244 | 0.97513 | 0.9285 | 0.8715 | 0.8171 | 0.77047 | 0.72124 | 0.6772 | 0.064826 | 0.044589 | 0.024352

## Slide 19: Effect of KnightShift on PG
20% Knight 50% Knight
KnightShift EP | 19
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
LOW(<50) | 0 | 0.072204 | 0.13845 | 0.2013 | 0.26239 | 0.3202 | 0.37647 | 0.43274 | -0.13517 | -0.048394 | 0.038385
MID(50-75) | 0 | 0.032603 | 0.066184 | 0.099045 | 0.1345 | 0.17513 | 0.22064 | 0.26968 | -0.13517 | -0.05703 | 0.021113
HIGH(75+) | 0 | 0.018621 | 0.022392 | 0.027864 | 0.035904 | 0.062013 | 0.098872 | 0.14383 | -0.13517 | -0.059771 | 0.015631
KnightShift effectively close the proportionality gap
at low utilization
Chart: Utilization
| 1.0 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0.0
LOW(<50) | 0 | 0.072204 | 0.13845 | 0.2013 | 0.26239 | -0.19221 | -0.11732 | -0.04243 | 0.032463 | 0.10735 | 0.18225
MID(50-75) | 0 | 0.032603 | 0.066184 | 0.099045 | 0.1345 | -0.19221 | -0.13372 | -0.075231 | -0.01674 | 0.041752 | 0.10024
HIGH(75+) | 0 | 0.018621 | 0.022392 | 0.027864 | 0.035904 | -0.19221 | -0.13893 | -0.085642 | -0.032356 | 0.02093 | 0.074216

## Slide 20: Effect of KnightShift on EP and LD
KnightShift essentially shifted all servers to –LD
All servers now have EP>60% (from 20%)
Some servers with EP=1
  KnightShift can achieve ideal EP!
KnightShift EP | 20
Chart: Linear Deviation
 | 0 | 3
Chart: 
 | 0 | 3

## Slide 21: Prototype Evaluation
Primary Server
  Dual 4-core Intel Xeon L5630
  500GB HD, 36GB DRAM
  156W-205W
  Sleep/Wakeup time 5/20s
Knight
  Intel Atom D525 (15% capable)
  500GB HD, 1GB DRAM
  15W-16.7W
EP improved from 24% to 48%
Evaluation | 21

## Slide 22: Prototype Evaluation
Wikipedia-based benchmark (WikiBench)[3]
  Cloned Wikipedia database dump
  Request trace from actual Wikipedia traffic
Evaluation | 22
[3]Wikibench – http://www.wikibench.eu

## Slide 23: Prototype Results
Evaluation | 23
High power usage during high utilization
Knight saves significant power during low utilization
Queuing model simulation
Sensitivity Analysis
  Utilization patterns
  Knight capability
  Transition time

## Slide 24: Conclusion
EP growth stalled by DR
Large disproportionality at low utilization
Key to improving EP
  Improve LD
  Target low utilization proportionality gap
  Need for server-level active low power mode
KnightShift exploits low utilization periods using a Knight
  Enables high efficiency at low utilization
  Effectively improves DR, LD and closes PG gap at low util.
  In some cases, achieves ideal EP
Conclusion | 24

## Slide 25
Thank you!
Questions?
Conclusion | 25