## Slide 1: CoScale: Coordinating CPU and Memory System DVFS in Server Systems
Qingyuan Deng, David Meisner+, Abhishek Bhattacharjee, Thomas F. Wenisch*, and Ricardo Bianchini
Rutgers University +Facebook Inc. *University of Michigan

## Slide 2: Server power challenges
CPU and memory power represent the vast majority of server power
Chart: Power Breakdown
| ILP | MID | MEM | MIX
CPU | 0.68441 | 0.54723 | 0.30182 | 0.50256
Memory | 0.22638 | 0.27803 | 0.38763 | 0.30327
Others | 0.08919 | 0.08919 | 0.08919 | 0.08919
Notes: 2

## Slide 3: Need to conserve both CPU and memory energy
Related work
  Lots of previous CPU DVFS works
  MemScale: Active low-power modes for memory [ASPLOS11]
Uncoordinated DVFS causes poor behavior
  Conflicts, oscillations, unstable behavior
  May not generate the best energy savings
  Difficult to bound the performance degradation
Need coordinated CPU and memory DVFS to achieve best results
  Challenge: Constrain the search space to good frequency combinations

## Slide 4: CoScale: Coordinating CPU and memory DVFS
Key goal
  Conserve significant energy while meeting performance constraints
Hardware mechanisms
  New performance counters
  Frequency scaling (DFS) of the channels, DIMMs, DRAM devices
  Voltage & frequency scaling (DVFS) of memory controller, CPU cores
Approach
  Online profiling to estimate performance and power consumption
  Epoch-based modeling and control to meet performance constraints
Main result
  Energy savings of up to 24% (16% on average) within 10% perf. target;
  4% on average within 1% perf. target

## Slide 5: Outline
Motivation and overview
CoScale
Results
Conclusions

## Slide 6: CoScale design
6
Goal: Minimize energy under user-specified performance bound
Approach: epoch-based OS-managed CPU / mem freq. tuning
Each epoch (e.g., an OS quantum):
  Profile performance & CPU/memory boundness
    Performance counters track mem-CPI & CPU-CPI, cache performance
  Efficiently search for best frequency combination
    Models estimate CPU/memory performance and power
  Re-lock to best frequencies; continue tracking performance
    Slack: delta between estimated & observed performance
  Carry slack forward to performance target for next epoch
Notes: 6

## Slide 7: Frequency and slack management
7
7
Time
Epoch 1
Epoch 2
Epoch 3
Epoch 4
High Mem Freq.
Low Mem Freq.
MC, Bus + DRAM
Core
Pos. Slack
Neg. Slack
Pos. Slack
Profiling
Target
Actual
Calculate slack vs. target
Estimate performance/energy via models
Low Core Freq.
High Core Freq.
Performance
Notes: 7

## Slide 8: Frequency search algorithm
Core 1 Frequency
Core 0 Frequency
Memory Frequency
Offline
O () : M: number of memory frequencies
C: number of CPU frequencies
N: number of CPU cores
Impractical!

## Slide 9: Frequency search algorithm
Core 1 Frequency
Core 0 Frequency
Memory Frequency
CoScale
O ()
Mem
Core 0
Core 1
Action
Metric: △Power/△Performance
0.73
0.65
0.81
Core 1
0.65
Mem
0.61
0.73
0.52
0.65
0.52
Mem
Core 0
Core 0
Mem
Mem
Core 1
Core grouping: Balance impact of memory and cores

## Slide 10: Outline
10
Motivation and overview
CoScale
Results
Conclusions

## Slide 11: Methodology
Detailed simulation
  16 cores, 16MB LLC, 4 DDR3 channels, 8 DIMMs
  Multi-programmed workloads from SPEC suites
Power modes
  Memory: 10 frequencies between 200 and 800 MHz
  CPU: 10 frequencies between 2.2GHz and 4GHz
Power model
  Micron’s DRAM power model
  McPAT CPU power model

## Slide 12: Results – energy savings and performance
Higher CPU energy savings on MEM; higher memory savings on ILP
System energy savings of 16% (up to 24%); always within perf. bound
Average energy savings
Performance overhead
Chart: 
| MEM | MID | ILP | MIX | AVG
Full system energy | 0.12118 | 0.15858 | 0.22697 | 0.1489 | 0.16391
Memory energy | 0.02845 | 0.20062 | 0.5308 | 0.14815 | 0.22701
CPU energy | 0.31898 | 0.18143 | 0.1687 | 0.19517 | 0.21607
Chart: 
| MEM | MID | ILP | MIX | AVG
Multiprogram average | 0.09075 | 0.0978 | 0.096725 | 0.096825 | 0.095525
Worst program in mix | 0.0983 | 0.1026 | 0.0999 | 0.1009 | 0.099088

## Slide 13: Alternative approaches
Memory system DVFS only: MemScale
CPU DVFS only
  Select the best combination of core frequencies
Uncoordinated
  CPU & memory DVFS controllers make independent decisions
Semi-coordinated
    CPU & memory DVFS controllers coordinate by sharing slack
Offline
  Select the best combination of memory and core frequencies
  Unrealistic: the search space is exponential on the number of cores

## Slide 14: Results – dynamic behavior
Chart: (a) CoScale
memory frequency | 0.8 | 0.533 | 0.533 | 0.467 | 0.467 | 0.467 | 0.467 | 0.467 | 0.4 | 0.6 | 0.467 | 0.467 | 0.4 | 0.467 | 0.533 | 0.667 | 0.533 | 0.533 | 0.533 | 0.533 | 0.533 | 0.533 | 0.533
core frequency | 4 | 3.46 | 3.46 | 3.82 | 3.64 | 3.64 | 3.64 | 3.82 | 3.82 | 3.46 | 3.64 | 3.82 | 3.82 | 3.64 | 3.46 | 3.1 | 3.28 | 3.46 | 3.46 | 3.28 | 3.46 | 3.46 | 3.28
Chart: (c) Semi-Coordinated
 | 0.8 | 0.333 | 0.8 | 0.467 | 0.8 | 0.4 | 0.8 | 0.4 | 0.8 | 0.467 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8 | 0.8
 | 4 | 3.28 | 4 | 3.28 | 4 | 3.28 | 4 | 3.1 | 4 | 2.92 | 3.82 | 3.1 | 3.28 | 3.28 | 2.56 | 2.92 | 2.74 | 2.74 | 2.74 | 2.56 | 2.56 | 2.56 | 2.74
Chart: (b) Uncoordinated
 | 0.8 | 0.467 | 0.4 | 0.4 | 0.467 | 0.4 | 0.4 | 0.467 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.533 | 0.533 | 0.533 | 0.533 | 0.533 | 0.533 | 0.533 | 0.533 | 0.533 | 0.533
 | 4 | 3.4 | 3 | 3.2 | 3.2 | 3.4 | 3.2 | 3.2 | 3.2 | 3.2 | 3.2 | 3.4 | 3.2 | 3.2 | 3.2 | 2.8 | 2.8 | 2.8 | 2.8 | 2.8 | 2.6 | 2.8 | 2.6 | 2.4 | 2.6
Timeline of milc application in MIX2

## Slide 15: Results – comparison to alternative approaches
Performance overhead
Full-system energy savings
Energy Savings (%)
CPI increase (%)
CoScale achieves comparable energy savings to Offline
Uncoordinated fails to bound the performance loss
Chart: 
| MemScale | CPUOnly | CoScale | Offline | Uncoord | Semi-coord
Full system energy | 0.081487 | 0.10108 | 0.16391 | 0.16691 | 0.18521 | 0.12687
Chart: 
| MemScale | CPUOnly | CoScale | Offline | Uncoord | Semi-coord
Multiprogram Average | 0.025325 | 0.096188 | 0.095525 | 0.095394 | 0.1227 | 0.096088
Worst in Mix | 0.0849 | 0.1042 | 0.1033 | 0.1026 | 0.1914 | 0.103

## Slide 16
Results – Sensitivity Analysis
Impact of performance bound
Chart: 
| System Energy Reduction | Worst Perf. Degradation
1% Bound | 0.036325 | 0.0094
5% Bound | 0.092825 | 0.0506
10% Bound | 0.15858 | 0.1019
15% Bound | 0.20838 | 0.15048
20% Bound | 0.24085 | 0.20185
Results for MID workloads

## Slide 17: Conclusions
CoScale contributions:
  First coordinated DVFS strategy for CPU and memory
  New perf. counters to capture energy and performance
  Smart OS policy to choose best power modes dynamically
Avg 16% (up to 24%) full-system energy savings
Framework for coordination of techniques across components
In the paper
  Details of search algorithm, performance counters, models
  Sensitivity analyses (e.g., rest-of-system power, prefetching)
  CoScale on in-order vs out-of-order CPUs

## Slide 18: THANKS!
SPONSORS: