## Slide 1: CoLT: Coalesced Large-Reach TLBs
December 2012
Binh Pham§, Viswanathan Vaidyanathan§, Aamer Jaleelǂ, Abhishek Bhattacharjee§
§Rutgers University ǂVSSAD, Intel Corporation

## Slide 2: Address Translation Primer
LSQ
Last Level Cache
LSQ
8 PTEs
L1 TLB
L2 TLB
L1 TLB
L2 TLB
L1 Cache
On a TLB miss:
x86: 1-4 memory references
ARM: 1-2 memory references
Sparc: 1-2 memory references

## Slide 3: Address Translation Performance Impact
Address translation performance overhead – 10-15%
  Clark & Emer [Trans. On Comp. Sys. 1985]
  Talluri & Hill [ASPLOS 1994]
  Barr, Cox & Rixner [ISCA 2011]
Emerging software trends
  Virtualization 2D walks – 89% overheads [Bhargava et al., ASPLOS 2008]
Emerging hardware trends
  LLC capacity to TLB capacity ratios increasing
  Manycore/hyperthreading increases TLB and LLC PTE stress

## Slide 4: Contiguity & CoLT
Page Table | 
Virtual | Physical
0 | 512
1 | 513
… | …
511 | 1023
512 | 1027
513 | 1025
514 | 1030
515 | 1031
516 | 1032
512 | 1027
High contiguity
Large pages
Low contiguity
TLB organization
Prefetching
Intermediate contiguity
CoLT
Low HW/SW
Eliminate 40-50% TLB misses
14% performance gain
TLB for large pages | 
Virtual | Physical
0 : 511 | 512 : 1023
TLB | 
Virtual | Physical
512 | 1027
513 | 1025
514 | 1030
515 | 1031
Coalesced TLB | 
Virtual | Physical
512 | 1027
513 | 1025
514:516 | 1030:1032
513 | 1025

## Slide 5: Intermediate Contiguity: Past Work and Our Goals
Past work
  TLB sub-blocking: Talluri & Hill [ASPLOS 94]
  SpecTLB: Barr, Cox & Rixner [ISCA 2011]
  Overheads from either HW or SW
  Alignment and special placement
CoLT goals:
  Low overhead HW
  No change in SW
  No alignment

## Slide 6: Outline
Intermediate contiguity:
  Why does it exist?
  How much exists in real systems?
  How do you exploit it in hardware?
  How much can it improve performance?
Conclusion

## Slide 7: Why does Intermediate Contiguity Exist?
Buddy allocator
Memory compaction
PFN 7
PFN 6
PFN 5
PFN 4
PFN 3
PFN 2
PFN 1
PFN 0
List 3
List 2
List 1
List 0
PFN 1
PFN 6/7
PFN 7
PFN 6
PFN 5
PFN 4
PFN 3
PFN 2
PFN 1
PFN 0
Moveable Pages
Free Pages
PFN 0/1/2/3
Free Lists
Physical Memory
PFN 4

## Slide 8: Real System Experiments
Study real system contiguity by varying:
  Superpage on or off
  Memory compaction daemon invocations
  System load
Real system configuration:
  CPU: Intel Core i7, 64 entry L1 TLBs, 512 entry L2 TLB
  Memory: 3 GB
  OS: Fedora 15, kernel 2.6.38

## Slide 9: How Much Intermediate Contiguity Exists?
295
56
150
84
83:117
Chart: 
| Tigr | Cact. | Milc | Mcf | Astar | Xalanc. | Bzip2 | Avg. (14)
No Memhog | 55.55 | 149.7 | 84.09 | 20.3 | 3.89 | 1.88 | 82.74 | 41.19
Memhog (25) | 42.6 | 41.2 | 11.24 | 295 | 10.14 | 1.6 | 117.5 | 43.37
Memhog (50) | 6.35 | 24.75 | 5.43 | 32.4 | 4.29 | 1.87 | 19.65 | 8.85
Exploitable contiguity across all system configurations
Not enough for superpages

## Slide 10: How do you Exploit it in Hardware?
Virtual | Physical
0 | 10
1 | 11
2 | 20
3 | 21
4 | 22
5 | 23
Reference Stream
Page Table
0
1
2
3
4
5
0
1
2
3
4
5
Standard
Coalesced
Virtual: 0 – 0b000
Virtual: 0 – 0b000
LLC
LLC
Coalescing Logic
PTEs for VPN 0 to 7
PTEs for VPN 0 to 7
Miss 1!
Miss 1!
0, 10
0,10: 1,11
Virtual: 1 – 0b001
Virtual: 1 – 0b001
Miss 2!
Virtual: 2 – 0b010
Virtual: 2 – 0b010
Miss 2!
Miss 3!
Virtual: 3 – 0b011
Virtual: 3 – 0b011
Miss 4!
3, 21
Virtual: 4 – 0b100
Virtual: 4 – 0b100
Miss 3!
Miss 5!
1, 11
2, 20
4, 22
Miss 12!
2, 20
5, 23
Virtual: 5 – 0b101
Virtual: 5 – 0b101
2,20:
3,21
4,22: 5,23
3, 21
4, 22

## Slide 11: CoLT for Set Associative TLBs
Hardware complexity
  Modest lookup complexity
  No additional ports
  Coalesce on fill to reduce overhead
  No additional page walks
Lookup for virtual page: 5 – 0b 1 0 1
Tag | Valid | Valid | Attribute | Base physical
0b1 | 1 | 1 | … | 0b10110
LLC
PTEs for VPN 0 to 7
Coalescing Logic
TLB
Tag | Valid | Valid | Attribute | Base physical
0b1 | 1 | 1 | … | 0b10110
Tag | Valid | Valid | Attribute | Base physical
0b1 | 1 | 1 | … | 0b10110
Tag | Valid | Valid | Attribute | Base physical
0b1 | 1 | 1 | … | 0b10110
Tag | Valid | Valid | Attribute | Base physical
0b1 | 1 | 1 | … | 0b10110
Combinational logic to calculate physical page

## Slide 12: CoLT Set Associative Miss Rates
Chart: % Misses Eliminated
| 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | Mcf | Tigr | Mumm. | Cact. | Astar | Omnet. | Xalanc.
L1 | 1.2534 | 21.8308 | 22.1287 | 6.6317 | 11.452 | 14.3846 | 5.35 | 9.6624 | 13.4813 | 52.8321 | 63.478 | -5658.4698 | 62.6261 | 87.3135 | 93.8448 | 6.7512 | 24.1348 | 62.4915 | 70.4002 | 98.9875 | 90.669
L2 | 1.2387 | 45.5317 | 9.0682 | 2.301 | 8.7053 | 14.0404 | 2.6812 | 8.6481 | 16.2439 | 54.6196 | 61.0054 | 26.087 | 82.8553 | 96.3074 | 95.9134 | 21.7916 | 27.941 | 20.123 | 35.2648 | 49.922 | 56.9565
Chart: % Misses Eliminated
| 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | 1 | 2 | 3 | Povray | Gems. | Gobmk | Fasta. | Sjeng | Bzip2 | Milc | Avg.
L1 | 16.5365 | 27.5759 | -14.2579 | 72.7434 | 82.5593 | 73.7726 | 21.7712 | 16.2362 | -21.7712 | 29.1656 | 22.6933 | -17.6969 | 13.3333 | 15.619 | 14.4762 | 22.7639 | 39.8886 | 40.4863 | 82.2116 | 98.9103 | 96.8443 | 33.1693 | 44.3101 | -370.6869
L2 | 16.3828 | 20.2949 | -125.0568 | 41.0789 | 40.4845 | 52.3778 | 5.5556 | 5.5556 | -694.4444 | 28.3929 | 62.3326 | -284.9406 | -145.4545 | 27.2727 | -972.7273 | 36.3077 | 52.4641 | 3.495 | 22.4804 | 58.2549 | 78.7843 | 14.6783 | 40.3371 | -121.72
Left-shifting 2 index bits best coalescing, conflict miss compromise
Roughly 50% average miss eliminations

## Slide 13: Different CoLT Implementations
Set-associative TLBs (CoLT-SA)
  Low hardware but caps coalescing opportunity
Fully-associative TLB (CoLT-FA)
  No indexing scheme – high coalescing opportunity
  More complex hardware – we use ½ baseline TLB size
Hybrid scheme (CoLT-All)
  CoLT-SA for limited coalescing
  CoLT-FA for high coalescing

## Slide 14: How Much Can it Improve Performance?
Chart: Perf. Improvement
| Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Mcf | Cact. | Astar | Omnet. | Xalanc. | Povray
 | 13.2 | 7.24 | 7.12 | 9.32 | 17.4 | 11.63 | 11.82 | 12.42 | 13.3 | 12.6 | 13 | 13 | 19.4 | 6.7 | 12.3 | 8.2 | 114.45 | 58 | 60 | 63 | 12.8 | 6.7 | 8.1 | 7.7
Chart: Perf. Improvement
| Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Perfect | CoLT-SA | CoLT-FA | CoLT-All | Gems. | Gobmk | Sjeng | Bzip2 | Milc | Avg.
 | 8 | 4 | 5.1 | 4.8 | 4.8 | 1.4 | 2.2 | 1.9 | 3.6 | 1.2 | 2.1 | 1.5 | 18.8 | 8.1 | 11.8 | 12.4 | 10.1 | 6.1 | 8.3 | 6.8 | 21.4409 | 11.2427 | 12.8945 | 12.8218
CoLT gets us half-way to a perfect TLB’s performance

## Slide 15: Conclusions
Buddy allocator, memory compaction, large pages, system load create intermediate contiguity
CoLT uses modest hardware to eliminate 40-50% TLB misses
Average performance improvements of 14%
CoLT suggests:
  Re-examining highly-associative TLBs?
  CoLT in virtualization? How hypervisor allocates physical memory?

## Slide 16
Thank you!

## Slide 17: Impact of Increasing Associativity
Chart: %Misses Eliminated
| Mcf | Tigr | Mumm. | Cact. | Astar | Omnet. | Xalanc.
4-way, CoLT-SA | 45.5317 | 8.7053 | 8.6481 | 61.0054 | 96.3074 | 27.941 | 44.5252
8-way, No CoLT | 1.723 | -0.19612 | -0.64673 | 37.0924 | -2.8251 | 8.9774 | 1.1985
8-way, CoLT-SA | 55.7297 | 8.9737 | 8.503 | 71.0598 | 99.5367 | 53.957 | 44.5252
Chart: %Misses Eliminated
| Povray | Gems. | Gobmk | Fasta. | Sjeng | Bzip2 | Milc | Avg.
4-way, CoLT-SA | 20.2949 | 40.4845 | 5.6 | 62.3326 | 27.3 | 52.4641 | 58.2549 | 39.9568
8-way, No CoLT | 8.5982 | 4.3851 | 16.6667 | 38.4732 | 63.6364 | 4.3578 | 0 | 12.96
8-way, CoLT-SA | 50.0739 | 53.5012 | 61.1111 | 74.0422 | 81.8182 | 60.9336 | 58.2549 | 55.8586
Notes: Normally, increasing associativity will come at the cost of higher look up time, and higher power consumption. Furthermore, increasing associativity say from 4 – 8 may increase the TLB miss rate very little, which is normally offset by the look up time and power consumption. (TODO: Look up the paper that talks about this). Therefore, in this experiment, we see if increasing the associativity and apply CoLT can give us higher incentive for doing so? As it is shown in the result, increasing 4 -> 8 only improve the miss rate by 10% in average, this is even lower than using CoLT at assoc = 4, and at assoc = 8, CoLT, we see close to 55% improvement in TLB miss rate.

## Slide 18: Comparison with Sub-blocking
Sub-blocking
  Uses a TLB entry to keep information about multiple mappings
  Complete Sub-blocking: no OS modification, big TLB
  Partial Sub-blocking: OS modification, small TLB, special placement required, e.g: VPN(x) / N = VPN(y) / N; PPN(x) / N = PPN(y) / N; VPN(x) % N = PPN(x) % N; VPN(y) % N = PPN(y) % N
CoLT
  NO alignment, special placement required
  Low overhead hardware, no overhead software