## Slide 1
independent work in between
Control-Flow Decoupling
Rami Sheikh, James Tuck, Eric Rotenberg North Carolina State University
Motivation
Single-thread performance is important for single- and multi-threaded applications.
Per-core energy consumption is at a premium.
Better branch handling is a BIG win: improves performance, reduces energy and enables memory latency tolerance.
CFD Compiler Implementation in GCC
Conclusion
A third of mispredictions come from separable branches.
CFD is a software/hardware collabor-ation for exploiting separability with low complexity and high efficacy.
CFD is comparable to if-conversion in terms of number of static branches and MPKI contribution.
Chart: Window Size
| 96 | 128 | 168 | 192 | 256 | 384 | 512
baseline | 0.70147 | 0.71762 | 0.72791 | 0.73067 | 0.73769 | 0.73858 | 0.73798
baseline + perfect prediction | 1.3155 | 1.4957 | 1.6952 | 1.8117 | 2.0677 | 2.4339 | 2.5856
Conroe
Nehalem
Sandy
Bridge
Haswell
Future Generations
Control-Flow Decoupling (CFD)
Key idea: separate the loop into two loops:
The first contains only the branch’s predicate computation.
The second contains the branch and its control-dependent instructions.
Results
Applying CFD manually:
Applying CFD automatically (compiler):
Chart: Normalized Energy
| eclat | jpeg-compr | mcf | soplex(pds) | soplex(ref) | tiff-2-bw
Manual | 0.60767 | 0.85229 | 0.91225 | 0.91651 | 0.79233 | 0.95
Automated | 0.61317 | 0.87332 | 0.963 | 0.92611 | 0.94064 | 0.96633
Chart: Speedup
| eclat | jpeg-compr | mcf | soplex(pds) | soplex(ref) | tiff-2-bw
Manual | 1.4301 | 1.1703 | 1.0187 | 1.0718 | 1.1333 | 1.056
Automated | 1.3984 | 1.1112 | 1 | 1.0346 | 1.0256 | 1.0308
hlin | 1 | 1
IDENTIFY
Branch slice
CLONE LOOP
Connect loop exits to the clone’s pre-header (provide in-order fetch)
INSERT
PUSH in loop: after branch slice
CLEAN-UP
Control-dependent region
POP in clone: to replace the branch
Dead and redundant code elimination
Interesting Observation
A third of mispredictions come from separable branches:
The branch has a large CD region (if-conversion not profitable).
The branch does not depend on its own CD instructions via a loop-carried data dependence.
branch-slice
control-
dependent
region
branch
63%
65%
67%
68%
69%
67%
65%
Energy Reduction
CFD
ISA Support
BQ specification
New push/pop instructions
Software Side
BQ size is finite + loops with high trip counts = loop strip-mining
Hardware Side
BQ microarch., length and recovery
Interaction with pipelining and OoO execution
BQ
CFD Loops
branch-slice
control-
dependent
region
branch
control-
dependent
region
branch-slice
branch
branch-slice
Push_BQ
control-
dependent
region
Branch_on_BQ
Original Loop
BQ drives fetch
IF
………….…
EX
IF
BQ miss
IF
………...
EX
IF
BQ hit
Common Case
Uncommon Case
Speculate or Stall
slice
branch
slice
branch
Execution Scenarios
Other interesting aspects of CFD:
Supports partially separable branches
Supports nested branches through multi-level decoupling
Overheads can be significantly reduced through value communication (called CFD+ in the paper)
Problem #2
No mechanism to comm. predicates to Fetch Unit
…..…
…..…..….
…..…..….
…..…..….
…..…..….
Problem #1
No fetch separation: need branch prediction
Original
…..…..….
…..…..….
IF
EX
IF
EX
…..…
IF
EX
IF
EX
slice
branch
slice
branch
CFD
…..…..….
IF
EX
IF
EX
slice
branch
…..…..….
IF
EX
slice
IF
EX
slice
IF
EX
branch
IF
EX
branch
CFD provides:
Fetch separation
Mechanism to comm. predicates to Fetch Unit
…….….
BQ