## Slide 1
Amoeba-Cache
Adaptive Blocks for Eliminating Waste in the Memory Hierarchy
Snehasish Kumar
Arrvindh Shriraman
Eric Matthews
Lesley Shannon
Hongzhou Zhao
Sandhya Dwarkadas

## Slide 2
Fixed granularity cache organisation
Tag Array
Data Array
Notes: Storage as 2D structure
Arranged as rows and columns
Rows are sets
Set has Cache blocks
Design parameters are fixed and inflexible
Tag array used for to check for data present in the cache

## Slide 3
Cache data utilization
Tags
Data
Untouched
Data
Tag Array
Data Array
Utilization = Fraction of words touched in cache block at the time of eviction
Notes: Segment the cache blocks into words
Data touched by the application shown in green
Waste in the form of untouched data at the time of eviction
Define utilization

## Slide 4
Chart: 64K L1 – 4 ways – 64B/block
Cache Utilisation | 0.29318 | 0.29821 | 0.31926 | 0.38465 | 0.39676 | 0.44811 | 0.45794 | 0.48563 | 0.52605 | 0.80186
apache
cann.
eclipse
firefox
h2
jbb
lbm
mcf
tpcc
x264
Cache utilization
Notes: 10 selected workloads
Talk about overall utilization
Explain groups – we do so because they show similar behaviour and present us with similar opportunities for optimisation

## Slide 5
Chart: 
| 1-2 Words | 3-4 Words | 5-6 Words | 7-8 Words
Sales | 55.1087 | 12.9481 | 6.3492 | 25.5939
Chart: 
| 1-2 Words | 3-4 Words | 5-6 Words | 7-8 Words
Sales | 18.1795 | 5.3767 | 3.814 | 72.6299
Block Distribution
1-2
3-4
5-6
7-8
Chart: 
| 1-2 Words | 3-4 Words | 5-6 Words | 7-8 Words
Sales | 40.4469 | 25.7633 | 8.6233 | 25.1665
Chart: 
| 1-2 Words | 3-4 Words | 5-6 Words | 7-8 Words
Sales | 75.0504 | 13.9436 | 6.0078 | 4.9982
Apache
Eclipse
Firefox
Canneal
# Words Touched
64K – 64B/block
Notes: Distribution

## Slide 6
Chart: 
| 1-2 Words | 3-4 Words | 5-6 Words | 7-8 Words
Sales | 57.5143 | 19.8922 | 12.4695 | 10.124
Block Distribution
1-2
3-4
5-6
7-8
Chart: 
| 1-2 Words | 3-4 Words | 5-6 Words | 7-8 Words
Sales | 75.0504 | 13.9436 | 6.0078 | 4.9982
Canneal
Canneal
# Words Touched
64K – 64B/block
1M – 64B/block
Notes: Idea – if cache size increases – lifetime of line increases – utilization increases

## Slide 7
Application specific behaviour
  Inefficient data structure access patterns
Interaction with cache geometry
  Way conflicts reduce block lifetime and cause poor utilization
Factors affecting cache utilization

## Slide 8
Application Specific Behaviour
struct TIE {
long long X, Y, Z;
long long V, H;
long long data[3];
} Imperial[1024];
Data[3]
X
Y
H
Z
V
Access in a loop
Data Array
for (int i=0; i<1024; i++)
{
Imperial[i].X = …;
Imperial[i].Y = …;
Imperial[i].Z = …;
Imperial[i].V = …;
}

## Slide 9
Cache Geometry
Data Array – 4 ways
Problem : Lots of data map to same set
1
2
3
4
5
Notes: Number of ways in a fixed granularity cache are limited, if a lot of data maps to a few set then there will not be enough ways to accommodate the data, thus evicting them before they can be fully utilized
Note : Change the partially used block to remove confusion

## Slide 10
Shrinks effective cache space
Increases miss rate
Wastes on-chip bandwidth
Increases on-chip cache energy consumption
Implications
=
Notes: Remember what Viji said

## Slide 11
Miss
Rate
Space
Utilisation
Bandwidth
Amoeba
Cache
Target Metrics
Notes: We can visualise the 3 issues in this fashion, there has been previous work which target certain aspects but only the amoeba cache targets all of them at the same time.

## Slide 12
Variable Granularity Blocks
Tag Array
Data Array
How to support variable # of blocks / set ?
How to support variable granularity for each block?
Notes: Imagine for a minute
Non uniform structure difficult to store
Extra metadata overhead in the form of more tags
Set size are also unequall
2 key questions

## Slide 13
Our Approach : Amoeba Cache
Unified SRAM Array
Notes: Merge tags with variable granularity data
Note the colors – used throughout

## Slide 14
Amoeba Cache
Insert
Lookup
Partial Miss
Overheads

## Slide 15
SRAM Array
Region Tag
Start
End
1 word
1+ words
SRAM Array
Tag
Data Block
Bitmaps
0000
Valid?
Tag?
0000
0000
0000
0000
0000
0000
0000
Notes: Smallest granularity data brought into the cache is 1 word.
At any time no two consecutive words can be valid tags. – Crucial observation which we use in the lookup stage to reduce overhead
Next we will take a closer look at what a region is which we store in the tag.

## Slide 16
Tag - Regions
Memory
Region
RMAX
bytes
Region Tag
Byte
Start /
End
Set Index
3
64 bit address
Top
3
Notes: Ends of each amoeba block lie within region boundaries

## Slide 17
Example
struct TIE {
long long X, Y, Z;
long long V, H;
long long data[3];
} Imperial;
Imperial.X = … ;
Miss
Invoke Spatial Granularity Predictor
(PC/Region based)
Fetch
Tag
X
Y
Z
V

## Slide 18
00000000
Valid?
Tag?
Amoeba Cache – Insert (8words/set)
00000000
SRAM Array / Set
Miss
Insert 4+1 words
00000
substring()
1
Pos: 0
Tag
X
Y
Z
V

## Slide 19
00000000
Valid?
Tag?
Amoeba Cache – Insert (8words/set)
00000000
SRAM Array / Set
11111000
Tag
X
Y
Z
V
Refill
2
10000000
3
Tag
X
Y
Z
V

## Slide 20
Example
struct TIE {
long long X, Y, Z;
long long V, H;
long long data[3];
} Imperial;
Imperial.Y = … ;
Lookup Data from the cache
Data[3]
X
Y
H
Z
V
X
Y
Z
V
Tag
X
Y
Z
V

## Slide 21
Amoeba Cache – Lookup (8words/set)
Region
Tag
Set Index
Word (W)
Tag
X
Y
Z
V
SRAM Array / Set
10000000
2x1
2x1
2x1
2x1
Tag?
1
2
Region
==
Start ≤ W
End > W
Word Selector
Hit?
3
Tag
X
Y
Z
V
Output Buffer
Critical Path

## Slide 22
Partial Miss
Identify Sub-Blocks
Step 1 of 2
New
∩ Tags
1
MSHR
2
Evict Overlap
Fetch New
Tag
X
Y
Z
V
Tag
X
Y
Tag
V
H

## Slide 23
Partial Miss
Insert New Block
Step 2 of 2
MSHR
3
Allocate 6 words
Miss
4
5
Patch Missing ?’s
Tag
Occurs ≈ 5 in 1000 accesses
Tag
X
Y
Z
V
H
X
Y
?
V
H
Z
Notes: Change

## Slide 24
Hardware Overheads
SRAM Array
Metadata
0000
Valid?
Tag?
0000
0000
0000
0000
0000
Critical Path
Extra
Amoeba Critical Path
1 KB
Latency +4%
Notes: Why only 4%?
Latency dominated by wire logic, comparaters used synthesised in Synopsys and comes to 4%

## Slide 25
Evaluation
Parameters for latency and energy
Workloads

## Slide 26
Latency Parameters (cycles)
300
64K L1
1M LLC
CPU
1
3
20
Fixed Granularity
Amoeba Cache
1.04
Latency +4%

## Slide 27
On-Chip Energy Parameters (pJ)
64K L1
1M LLC
101
230
Fixed Granularity
Amoeba Cache
≈ 7 / word
105
238
Notes: Check on why the numbers are so different.

## Slide 28
22 diverse workloads from
  PARSEC
  SPEC-CPU 2000 & 2006
  DaCapo ( Java Benchmarks )
  Apache, Firefox and PostgreSQL
Workloads

## Slide 29
Results

## Slide 30
% Improvement in L1 Miss-Rate
Chart: 
| mcf | canneal | lbm | h2 | jbb | apache | x264 | firefox | tpcc | eclipse
Change | 0.2261 | 0.093467 | 0.032439 | 0.36058 | 0.13024 | 0.18041 | 0.13088 | 0.10056 | 0.17034 | 0.1531
Reduces L1 and L2 miss rate by 18%
Notes: Higher bars are better
Relate to grouping
Mcf – reduced pollution
H2 – reduced pollution – around 8-9 blocks per 256b set
Canneal, lbm – Streaming nature

## Slide 31
% Improvement in L1 Miss-Bandwidth
Chart: 
| mcf | canneal | lbm | h2 | jbb | apache | x264 | firefox | tpcc | eclipse
Change | 0.62978 | 0.44814 | 0.58883 | 0.57004 | 0.44906 | 0.4505 | 0.45112 | 0.32017 | 0.39587 | 0.20034
Reduces on-chip bandwidth by 46%
Reduces off-chip bandwidth by 38%
Notes: All workloads show improvement in bandwidth due to elimination of waste

## Slide 32
% Improvement in memory energy
Chart: 
| mcf | canneal | lbm | h2 | jbb | apache | x264 | firefox | tpcc | eclipse
Change | 0.35665 | 0.059703 | 0.26888 | 0.068275 | 0.093026 | 0.21007 | 0.047125 | 0.0098365 | 0.043274 | 0.025388
Reduces energy by 11%
Notes: Mcf, lbm, apache on enabling Amoeba fit in the 1M LLC, reducing off chip transfers and shows large energy savings

## Slide 33
% Improvement in execution time
Chart: 
| mcf | canneal | lbm | h2 | jbb | apache | x264 | firefox | tpcc | eclipse
Change | 0.11925 | 0.074964 | 0.046916 | 0.025724 | 0.21216 | 0.10631 | 0.024344 | 0.015315 | 0.033857 | 0.0079872
Improves performance by 10%
Notes: Combination of reduction of miss rate at L1 and LLC gives us improvement in execution time for jbb
Eclipse not affected as it’s a small application which fits into the cache at the LLC for Fixed gran and Amoeba

## Slide 34
Results Summary
Amoeba-Cache
  Reduce cache pollution for applications with low cache utilization
  Improve performance for moderate cache utilization
  Maintain performance for high cache utilization workloads
  Save energy for streaming applications by keeping out unused words

## Slide 35
Additional Results
Lookup as an extra cache pipeline stage vs. throttling the CPU
Spatial Granularity Predictor
  Indexing
  Training
  Table Size
For extra pipeline stage, 8 of 22 applications show improvement
18 of 22 – Address region better
Evictions and First Touch
256 – PC and 1024 – Region
Notes: Summarize each result here
Reduce the size of the list,

## Slide 36
Additional Results
Multicore Shared Cache
Comparison against other designs
  Fixed Granularity 2X
  Sector Cache variants
  Multi-$
Reduces miss rate (avg 18%) and LLC miss bandwidth (16%-39%)
Notes: Pop in chart over here? Na…

## Slide 37
Amoeba Cache
What?
  Enable variable granularity data caching
Why?
  Eliminate waste
How?
  Unify tag and data into a single SRAM array
    Afforded by recent technology trends
Where?
  Definitely at the L2, possibly at the L1

## Slide 38
Frequently Asked Questions
Multiple threads?
Compare against other designs
Spatial Pattern Predictor
Replacement Policy
Notes: Multiple threads? – 39
Compare against other designs – 40
Spatial Pattern Predictor – 42
Replacement Policy – 49

## Slide 39
Multicore Shared Cache
 | Miss | Miss | Miss | Miss | BW
Mix | T1 | T2 | T3 | T4 | (All)
jbb x2, tpc-c x2 | 12.38% | 12.38% | 22.29% | 22.37% | 39.07%
Firefox x2, x264 x2 | 3.82% | 3.61% | –2.44% | 0.43% | 15.71%
cactus, fluid., omnet., sopl. | 1.01% | 1.86% | 22.38% | 0.59% | 18.62%
canneal, astar, ferret, milc | 4.85% | 2.75% | 19.39% | –4.07% | 17.77%

## Slide 40
Comparison
Impact on Miss-Rate
Impact on Bandwidth
Low tag overhead
Tradeoff data and tag space
Dynamically resize blocks
Amoeba Cache
Multi -$
Sector Variants
Yes
Yes
~
~
No
Yes
No
No
No
No

## Slide 41
Comparison – Moderate Group – 64K
Chart: Miss Rate Ratio
| 1 | 1.0830435367084299 | 1.1156773585552799 | 1.2045080604227201 | 1.6 | 1.5388341947603901
 | 1 | 0.7065 | 0.57465 | 0.61651 | 0.84567 | 0.65854

## Slide 42
Spatial Pattern Predictor
Index | Pattern
PC / Region | 01011111
PC / Region | 00011101
Predictor History Table
1
PC : Read Addr
0
0
0
1
1
1
0
1
2
Critical Word
Policy Miss vs Policy-Bandwidth
What to do when there is no entry?

## Slide 43
Predictor Training
Data Array
Index | Pattern
PC / Region | 01011111
PC / Region | 00011101
Add / update entry on evict

## Slide 44
Predictor – L1 Miss Rate (1 of 2)
Chart: MPKI
| canne. | eclip. | firef. | h2 | tpc-c | x264
Aligned | 9.1183 | 4.2664 | 1.6241 | 7.1857 | 6.4734 | 4.7281
Finite | 9.4137 | 4.0698 | 1.6389 | 7.203 | 6.639 | 4.4924
Infinite | 9.8295 | 4.0698 | 1.6539 | 7.2044 | 6.6495 | 4.4936
Finite+FT | 9.1054 | 4.0595 | 1.6118 | 7.1928 | 6.6275 | 4.4816
History | 8.266 | 3.6132 | 1.4608 | 4.5947 | 5.3707 | 4.1093

## Slide 45
Predictor – L1 Miss Rate (2 of 2)
Chart: MPKI
| apac. | lbm | mcf | jbb
Aligned | 79.1701 | 65.1785 | 72.0364 | 28.2253
Finite | 80.4401 | 65.4392 | 69.6381 | 28.292
Infinite | 80.8583 | 67.8531 | 69.7673 | 28.3867
Finite+FT | 78.8835 | 64.945 | 69.1915 | 26.6034
History | 64.887 | 63.0642 | 55.7491 | 24.5492

## Slide 46
Predictor – L1 Miss Bandwidth (1 of 2)
Chart: Bandwidth Rate
| canne. | eclip. | firef. | h2 | tpc-c | x264
Aligned | 880.566 | 541.577 | 180.219 | 761.704 | 724.569 | 492.197
Finite | 852.788 | 505.386 | 171.609 | 691.984 | 695.167 | 414.769
Infinite | 842.081 | 505.386 | 171.25 | 691.839 | 695.366 | 414.597
Finite+FT | 667.656 | 504.135 | 155.962 | 688.458 | 686.823 | 407.118
History | 485.951 | 433.076 | 122.518 | 327.502 | 437.731 | 270.159

## Slide 47
Predictor – L1 Miss Bandwidth (2 of 2)
Chart: Bandwidth Rate
| apac. | lbm | mcf | jbb
Aligned | 9098.57 | 9131.9 | 6803.12 | 2798.93
Finite | 8297.99 | 8864.99 | 5406.59 | 2603.34
Infinite | 8188.41 | 8992.84 | 5212.89 | 2460.84
Finite+FT | 7722.84 | 5989.21 | 4908.15 | 1974.01
History | 4999.69 | 3754.79 | 2518.64 | 1542.05

## Slide 48
Predictor – Summary
For majority applications Region Predictor with
  1024 entry table
  Table with 8 ways x 128 sets
PC Predictor is good for 5 applications
  apache, art, mcf, lbm and omnetpp
Notes: Modeled in CACTI and can be indexed in 0.025ns and requires 2.3 pJ per indexing ( adds 0.12% energy )

## Slide 49
Pseudo LRU Replacement
Logically partition the set into a Nways
Pick a block at random from way
Unset the T? (Tag) and V? (Valid) bits
Way 0
Way 1

## Slide 50
Chart: Words Accessed (%)
| apache | art | astar | cactus | canneal | eclipse | facesim | ferret | firefox | fluid. | freq. | h2 | jbb | lbm | mcf | milc | omnet. | soplex | tpc-c. | trade. | twolf | x264 | mean
1-2 Words | 55.1087 | 88.0112 | 67.1341 | 23.4255 | 75.0504 | 18.1795 | 6.818 | 15.3913 | 40.4469 | 14.7216 | 47.7647 | 53.5734 | 64.492 | 76.8357 | 61.7963 | 14.5311 | 62.7431 | 93.1641 | 41.9657 | 24.0571 | 54.9813 | 51.0008 | 47.7815
3-4 Words | 12.9481 | 6.7355 | 6.3093 | 1.6136 | 13.9436 | 5.3767 | 20.6985 | 2.931 | 25.7633 | 18.5049 | 6.979 | 22.2848 | 11.5268 | 6.4011 | 30.1399 | 11.3718 | 22.8829 | 3.8375 | 15.2663 | 8.5313 | 42.5987 | 17.1377 | 14.2628
5-6 Words | 6.3492 | 0.00078523 | 5.8362 | 1.0613 | 6.0078 | 3.814 | 19.6343 | 10.3411 | 8.6233 | 62.4836 | 1.841 | 11.9557 | 3.6702 | 0.0090521 | 6.6538 | 11.1117 | 4.6695 | 0.72449 | 9.8063 | 4.6118 | 2.3862 | 5.1304 | 8.4873
7-8 Words | 25.5939 | 5.2525 | 20.7204 | 73.8996 | 4.9982 | 72.6299 | 52.8493 | 71.3365 | 25.1665 | 4.29 | 43.4154 | 12.1861 | 20.3111 | 16.7542 | 1.41 | 62.9854 | 9.7045 | 2.2739 | 32.9617 | 62.7998 | 0.033835 | 26.731 | 29.4683
Access Distribution for L1
Word distribution for 64K L1

## Slide 51
Amoeba block size distribution for L1
Block distribution for 64K L1
Chart: % of Amoeba Blocks
| apache | art | astar | cactus | canneal | eclipse | facesim | ferret | firefox | fluid. | freq. | h2 | jbb | lbm | mcf | milc | omnet. | soplex | tpc-c. | trade. | twolf | x264 | mean
1-2 Words | 40.9676 | 83.41 | 29.4509 | 10.9152 | 35.488 | 9.6514 | 5.9708 | 14.155 | 25.782 | 14.4627 | 40.1108 | 39.0993 | 52.6567 | 60.2229 | 51.7339 | 14.5261 | 44.982 | 88.0816 | 35.1254 | 15.2945 | 39.7511 | 46.8666 | 36.3048
3-4 Words | 14.1587 | 0.0085333 | 9.1816 | 1.7171 | 38.6832 | 3.3044 | 7.2719 | 2.1382 | 11.7211 | 18.6627 | 3.1352 | 15.7518 | 13.3747 | 10.6269 | 35.5303 | 11.3672 | 15.9943 | 3.5212 | 10.2039 | 4.6276 | 33.4003 | 6.623 | 12.3183
5-6 Words | 9.1139 | 7.6962 | 10.0958 | 0.22954 | 8.5166 | 2.4568 | 2.5146 | 10.481 | 13.2375 | 62.8235 | 3.0976 | 12.4796 | 6.6674 | 3.5431 | 8.9204 | 11.103 | 18.8511 | 3.5693 | 10.3555 | 4.2621 | 17.2964 | 4.0902 | 10.5182
7-8 Words | 35.7598 | 8.8853 | 51.2718 | 87.1382 | 17.3122 | 84.5874 | 84.2427 | 73.2259 | 49.2594 | 4.051 | 53.6564 | 32.6693 | 27.3012 | 25.6071 | 3.8154 | 63.0037 | 20.1726 | 4.8279 | 44.3153 | 75.8158 | 9.5522 | 42.4202 | 40.8587

## Slide 52
L1 FSM

## Slide 53
Miss-Rate ( 64K L1 )
Chart: 
| mcf | canneal | lbm | h2 | jbb | apache | x264 | firefox | tpcc | eclipse
Fixed | 72.0364 | 9.1183 | 65.1785 | 7.1857 | 28.2253 | 79.1701 | 4.7281 | 1.6241 | 6.4734 | 4.2664
Amoeba | 55.7491 | 8.266 | 63.0642 | 4.5947 | 24.5492 | 64.887 | 4.1093 | 1.4608 | 5.3707 | 3.6132

## Slide 54
Miss Bandwidth Rate ( 64K L1 )
Chart: 
| mcf | canneal | lbm | h2 | jbb | apache | x264 | firefox | tpcc | eclipse
Fixed | 6803.12 | 880.566 | 9131.9 | 761.704 | 2798.93 | 9098.57 | 492.197 | 180.219 | 724.569 | 541.577
Amoeba | 2518.64 | 485.951 | 3754.79 | 327.502 | 1542.05 | 4999.69 | 270.159 | 122.518 | 437.731 | 433.076

## Slide 55
Energy Rate ( L1 + LLC ) – (nJ/KI)
Chart: 
| mcf | canneal | lbm | h2 | jbb | apache | x264 | firefox | tpcc | eclipse
Fixed | 73.5104 | 45.9636 | 66.307 | 35.928 | 72.4411 | 101.5687 | 40.1931 | 44.8187 | 45.5684 | 40.3839
Amoeba | 47.2931 | 43.2195 | 48.4783 | 33.475 | 65.7022 | 80.2319 | 38.299 | 44.3778 | 43.5964 | 39.3587

## Slide 56
Reduction in execution time
Chart: 
| mcf | canneal | lbm | h2 | jbb | apache | x264 | firefox | tpcc | eclipse
Fixed | 14940.01 | 3501.95 | 14285.01 | 1841.87 | 6385.32 | 9286.34 | 2295.42 | 2151.5 | 2075.17 | 1801.64
Amoeba | 13158.48 | 3239.43 | 13614.81 | 1794.49 | 5030.6 | 8299.13 | 2239.54 | 2118.55 | 2004.91 | 1787.25