## Slide 1: Inferred Models for Dynamic and Sparse Hardware-Software Spaces
Weidan Wu, Benjamin C. Lee
Duke University

## Slide 2: Trends in Management & Diversity
Increasingly Sophisticated Management
  Allocate resources, schedule applications, …
  Understand HW-SW interactions
Increasingly Diverse HW & SW
  Heterogeneous cores, VMs, contention, …
  Diverse clients, jobs, tasks, …

## Slide 3: Mapping Software to Hardware
  Management space explosion (M x N)
Heterogeneous HW
Diverse SW
N
M
A HW-SW Mapping

## Slide 4: Profilers Support Management
  But profile sparsity increases with diversity
System Management Space
Sparse Samples
HW
SW

## Slide 5: Inference with Sparse Profiles
System Management Space
HW
SW

## Slide 6: Outline
Introduction
Inferred Performance Models
Generalized Models
Specialized Models
Conclusions

## Slide 7: Inferred Performance Models
  Models, predictions support management
System Management Space
HW
SW
Model

## Slide 8: Integrated HW & SW Analysis
  Lays a foundation for run-time management
  Increases diversity among sparse samples
  Prior work separates HW & SW
System Management Space
HW
SW

## Slide 9: New Challenges
Larger space, greater sparsity
  Data re-usability is critical
  30 parameters  5E+15 points
Less structured training data
  SW profiles from arbitrary, real shards
  HW profiles from defined, simulated design space

## Slide 10: Principles and Strategies
Enhance data re-usability
  Shard-level profiles
  Portable characteristics (μ-arch independent)
Automate modeling
  Genetic algorithm
  Mitigate space explosion

## Slide 11: Shard-level Profiles
Shards: short dynamic instruction segments
Re-use data among applications
  New shards resemble existing ones
  Monolithic profiles only useful when entire application resembles existing one
A Shard

## Slide 12: Shard-level Profiles
Shards are sparse, randomly sampled segments of 10M instructions
Shards from diverse applications complement each other, reducing profiling costs
Shards expose intra-application diversity

## Slide 13: Portable Characteristics
Re-use data among microarchitectures
  Microarchitecture-independent measures
  Ex: instruction mix versus cache miss rate
  Existing SW profiles relevant for new HW

## Slide 14: Sharing Supports Inference
Shards enhances data re-use across SW
Portability enhances data re-use across HW
Inferred models require less training data due to enhanced re-use

## Slide 15: Statistical Inference
CPI ALUs, cache size, … mem instr freq regression coefficients
X includes non-linear kernel transformations
  Ex: log(cache size)
X includes pair-wise interactions
  Ex: ALU instructions, units

## Slide 16: Space of Model Specifications
Many kernel transformations
  log, power, cubic spline, exponential, sqrt…
  30 parameters, 5 kernels  model specs
Many parameter interactions
  Hardware and software interact
  = 435 pairwise interactions  specs

## Slide 17: Automatic Model Construction
  Model specification encoded as genes
  Mutation, crossover search models
  Selection evolves model toward higher accuracy
Training Data
Genetic Algorithm
Model (kernels, interactions)

## Slide 18: Automatic Model Updates
  New data updates model specification
  Algorithm changes kernels, interactions, fit
New Training Data
Genetic Algorithm
Old Model
Model (kernels, interactions)

## Slide 19: Outline
Introduction
Inferred Performance Models
Generalized Models
Specialized Models
Conclusions

## Slide 20: Generalized Models
Diverse SW as applications enter/leave system
  Ex: democratized datacenter computing
Heterogeneous HW as architectures tuned
  Ex: big/small cores, VMs, contention, …
Profiled data collected as SW runs on HW
Models update to accommodate dynamics

## Slide 21: Inductive Hypothesis
  System in steady state
  Accurate model is trained M(H,S)
  Manager uses model predictions
model
system manager
scheduling

## Slide 22: Inductive Step
  System is perturbed with new SW or HW
  Profile new SW-HW, check prediction
Model
Accurate ?
Yes
No
Still in Steady State
System Manager
Update
New application

## Slide 23: Model Updates
Poor prediction triggers model update
  Collect a few profiles for new SW (e.g., 10-20)
  Update kernels, interactions, fit
New Training Data
Genetic Algorithm
Old Model
Model (Kernels, Interactions)

## Slide 24: Integrated HW & SW Space
  Hardware Space (17 parameters)
  Pipeline parameters  e.g. width, rob size
  Cache parameters  e.g., cache size, associativity
  Functional unit  e.g., ALU count
Software Space (13 parameters)
  Instruction mix
  Locality  e.g., re-use distance
  ILP  e.g., producer-consumer distance

## Slide 25: Steady State Interpolation
  Train model with sparse HW-SW profiles
  Interpolate for HW-SW pairs not profiles

## Slide 26: Perturbed Extrapolation
  Train model with sparse HW-SW profiles
  Extrapolate for new SW and new HW
  Predict app n from n-1 apps
  Also supports SW variants (compiler opt, data inputs)

## Slide 27: Relative Accuracy
  Accurate interpolation, extrapolation
  Correlation coefficient > 0.9

## Slide 28: Outline
Introduction
Inferred Performance Models
Generalized Models
Specialized Models
Conclusions

## Slide 29: Specialized Models
Generality is expensive
  Requires many SW characteristics (e.g,. 13)
With domain knowledge, SW behavior expressed at higher level
  Reduces number of SW characteristics
  Reduces profiling cost
  Increases model accuracy

## Slide 30: Sparse Matrix-Vector Multiply
  Compute y=Ax+b when A is sparse, blocked
  SW space  block row, block column, fill ratio
  HW space  cache

## Slide 31: SpMV Model Accuracy
  Models irregular performance caused by fill ratios
True performance
Predictive performance
Notes: Separate two figures

## Slide 32: Also in the paper…
Shard-level prediction
  Basis of application prediction
Genetic algorithm evaluation
  Convergence versus model accuracy
Coordinated optimization for SpMV
  Optimize HW and software
  Optimize performance and power

## Slide 33: Conclusions
Present framework to close data-to-decision gap
Infer performance from huge, sparse data
Automate modeling in dynamic managers
Apply domain knowledge for concise models

## Slide 34: Inferred Models for Dynamic and Sparse Hardware-Software Spaces
Weidan Wu, Benjamin C. Lee
Duke University