## Slide 1: DeSC: Decoupled Supply-Compute Communication Management for Heterogeneous Architectures
Tae Jun Ham (Princeton Univ.)
Juan Luis Aragón (Univ. of Murcia) Margaret Martonosi (Princeton Univ.)

## Slide 2: Accelerator Communication Challenge
  Limited scratchpad memory size
Best if data arrives at accelerator before computation needs it
Data should be carefully divided/blocked
Programmers manage accelerator communication
  Little memory latency tolerance
  Difficult and error-prone
  Limited portability across varying local memory sizes
  Often results in suboptimal performance
Problems
Accelerators require careful communication management
Current Solution

## Slide 3: DeSC Solution
DEcoupled Supply-Compute communication management (DeSC) automatically manages and optimizes accelerator communication
  Portability: work with any local memory size
  Performance: minimize the effect of memory latency by communicating data to local memory as early as possible
  Specialization: different HW could be used for comm. and comp.
Our Solution
  Limited scratchpad memory size
  Little memory latency tolerance
Problems
Accelerators require careful communication management
Best if data arrives at accelerator before computation needs it
Data should be carefully divided/blocked

## Slide 4: Decoupling Communication and Computation
Decoupling communication and computation is a key to DeSC’s communication management
  Inspired by James Smith’s seminal work “Decoupled Access/Execute Architecture”
Computation Slice
for (i=0;i<N;i++) { v1 = CONSUME(); v2 = CONSUME(); val = v1 + v2 * k; STORE_VAL(val) }
Original Code
for (i=0;i<N;i++) { v1 = LOAD(&a[i]); v2 = LOAD(&b[i]); val = v1 + v2*k; STORE(&c[i], val) }
Data Supply Slice
for (i=0;i<N;i++) { v1 = LOAD(&a[i]); PRODUCE(v1); v2 = LOAD(&b[i]); PRODUCE(v2); STORE_ADDR(&c[i]); }
Data Supply Slice: instructions to calculate the address for LOAD/STORE instructions & PRODUCE instructions
Computation Slice: instructions to compute the value for STORE instructions & CONSUME instructions

## Slide 5: DeSC: Decoupled Supply Compute Communication Management
DeSC is a HW/SW framework which automatically manages and optimizes communication through decoupling
LLVM-based DeSC compiler decouples software into data supply slice and computation slice
Each slice is mapped to a different specialized hardware (SuppD and CompD)
Supplier Side
Supplier Device (SuppD)
Computation Device (CompD)
LLVM DeSC Compiler Pass
Data Supply
Slice
Computation
Slice
Mem Interface
Compile-Time
Run-Time
Communication Queue
Computation Side
PRODUCE
CONSUME

## Slide 6: Key Benefits of DeSC
DeSC SuppD knows exact next data that will be used by CompD
DeSC SuppD can pass data to CompD before it actually needs it
DeSC allows use of specialized device for SuppD and CompD
Portability : DeSC can work with any given local storage (Comm. Queue) size
Performance: DeSC can minimize the memory latency exposed to the comp.
Specialization: DeSC utilizes an extended out-of-order core as SuppD and an accelerator or an out of order core as CompD

## Slide 7: Presentation Outline
Key optimizations of DeSC
Terminal load optimization
DeSC Evaluation Results
Conclusions
Loss of decoupling optimization

## Slide 8: Challenges in using OoO core as a SuppD
Challenge : Long latency load blocks the head of ROB
OoO SuppD |  |  |  |  |  | 
Cycle | Issue | Issue | ROB1 | ROB2 | ROB3 | ROB4
0 | LD A1 | LD B1 | LD A1 | LD B1 |  | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
7 |  |  |  |  |  | 
8 |  |  |  |  |  | 
9 |  |  |  |  |  | 
10 |  |  |  |  |  | 
11 |  |  |  |  |  | 
12 |  |  |  |  |  | 
13 |  |  |  |  |  | 
14 |  |  |  |  |  | 
Issue width = 2
ROB Size = 4
LD A latency = 6
LD B latency = 2
Example Simplified SuppD Slice
for (i=1;i<N;i++) { v1 = LOAD(&a[i]); v2 = LOAD(&b[i]); }
On cycle 0, the core will issue both LD A1 and LD B1.

## Slide 9: Challenges in using OoO core as a SuppD
Challenge : Long latency load blocks the head of ROB
OoO SuppD |  |  |  |  |  | 
Cycle | Issue | Issue | ROB1 | ROB2 | ROB3 | ROB4
0 | LD A1 | LD B1 | LD A1 | LD B1 |  | 
1 | LD A2 | LD B2 |  |  | LD A2 | LD B2
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
7 |  |  |  |  |  | 
8 |  |  |  |  |  | 
9 |  |  |  |  |  | 
10 |  |  |  |  |  | 
11 |  |  |  |  |  | 
12 |  |  |  |  |  | 
13 |  |  |  |  |  | 
14 |  |  |  |  |  | 
Issue width = 2
ROB Size = 4
LD A latency = 6
LD B latency = 2
Example Simplified SuppD Slice
for (i=1;i<N;i++) { v1 = LOAD(&a[i]); v2 = LOAD(&b[i]); }
On cycle 1, the core will issue LD A2 and LD B2.

## Slide 10: Challenges in using OoO core as a SuppD
Challenge : Long latency load blocks the head of ROB
OoO SuppD |  |  |  |  |  | 
Cycle | Issue | Issue | ROB1 | ROB2 | ROB3 | ROB4
0 | LD A1 | LD B1 | LD A1 | LD B1 |  | 
1 | LD A2 | LD B2 |  |  | LD A2 | LD B2
2 |  |  |  | Wait for Commit |  | 
3 |  |  |  |  |  | Wait for Commit
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
7 |  |  |  |  |  | 
8 |  |  |  |  |  | 
9 |  |  |  |  |  | 
10 |  |  |  |  |  | 
11 |  |  |  |  |  | 
12 |  |  |  |  |  | 
13 |  |  |  |  |  | 
14 |  |  |  |  |  | 
Issue width = 2
ROB Size = 4
LD A latency = 6
LD B latency = 2
Example Simplified SuppD Slice
for (i=1;i<N;i++) { v1 = LOAD(&a[i]); v2 = LOAD(&b[i]); }
LD B1 is finished but cannot commit because LD A1 didn’t commit

## Slide 11: Challenges in using OoO core as a SuppD
Challenge : Long latency load blocks the head of ROB
OoO SuppD |  |  |  |  |  | 
Cycle | Issue | Issue | ROB1 | ROB2 | ROB3 | ROB4
0 | LD A1 | LD B1 | LD A1 | LD B1 |  | 
1 | LD A2 | LD B2 |  |  | LD A2 | LD B2
2 | X | X |  | Wait for Commit |  | 
3 | X | X |  |  |  | Wait for Commit
4 | X | X |  |  |  | 
5 | X | X |  |  |  | 
6 |  |  |  |  |  | 
7 |  |  |  |  |  | 
8 |  |  |  |  |  | 
9 |  |  |  |  |  | 
10 |  |  |  |  |  | 
11 |  |  |  |  |  | 
12 |  |  |  |  |  | 
13 |  |  |  |  |  | 
14 |  |  |  |  |  | 
Issue width = 2
ROB Size = 4
LD A latency = 6
LD B latency = 2
Example Simplified SuppD Slice
for (i=1;i<N;i++) { v1 = LOAD(&a[i]); v2 = LOAD(&b[i]); }
No instruction will be issued until the end of Cycle 5.

## Slide 12: Challenges in using OoO core as a SuppD
Challenge : Long latency load blocks the head of ROB
OoO SuppD |  |  |  |  |  | 
Cycle | Issue | Issue | ROB1 | ROB2 | ROB3 | ROB4
0 | LD A1 | LD B1 | LD A1 | LD B1 |  | 
1 | LD A2 | LD B2 |  |  | LD A2 | LD B2
2 | X | X |  | Wait for Commit |  | 
3 | X | X |  |  |  | Wait for Commit
4 | X | X |  |  |  | 
5 | X | X |  |  |  | 
6 |  |  |  |  |  | 
7 |  |  |  |  |  | 
8 |  |  |  |  |  | 
9 |  |  |  |  |  | 
10 |  |  |  |  |  | 
11 |  |  |  |  |  | 
12 |  |  |  |  |  | 
13 |  |  |  |  |  | 
14 |  |  |  |  |  | 
Issue width = 2
ROB Size = 4
LD A latency = 6
LD B latency = 2
A1, B1
A2, B2
Example Simplified SuppD Slice
for (i=1;i<N;i++) { v1 = LOAD(&a[i]); v2 = LOAD(&b[i]); }
Data will be communicated to the Comm. Queue when they commit

## Slide 13: Challenges in using OoO core as a SuppD
Challenge : Long latency load blocks the head of ROB
OoO SuppD |  |  |  |  |  | 
Cycle | Issue | Issue | ROB1 | ROB2 | ROB3 | ROB4
0 | LD A1 | LD B1 | LD A1 | LD B1 |  | 
1 | LD A2 | LD B2 |  |  | LD A2 | LD B2
2 | X | X |  | Wait for Commit |  | 
3 | X | X |  |  |  | Wait for Commit
4 | X | X |  |  |  | 
5 | X | X |  |  |  | 
6 | LD A3 | LD B3 | LD A3 | LD B3 |  | 
7 | LD A4 | LD B4 |  |  | LD A4 | LD B4
8 | X | X |  | Wait for Commit |  | 
9 | X | X |  |  |  | Wait for Commit
10 | X | X |  |  |  | 
11 | X | X |  |  |  | 
12 | LD A5 | LD B5 | LD A5 | LD B5 |  | 
13 | LD A6 | LD B6 |  |  |  | 
14 | X | X |  |  |  | 
Issue width = 2
ROB Size = 4
LD A latency = 6
LD B latency = 2
A1, B1
A2, B2
A3, B3
A4, B4
Example Simplified SuppD Slice
for (i=1;i<N;i++) { v1 = LOAD(&a[i]); v2 = LOAD(&b[i]); }

## Slide 14: Challenges in using OoO core as a SuppD
DeSC Question : Why should LD B should wait until former long latency LD A commits?
SuppD |  |  | 
ROB1 | ROB2 | ROB3 | ROB4
LD A1 | LD B1 |  | 
 |  | LD A2 | LD B2
 | Wait for Commit |  | 
 |  |  | Wait for Commit
LD A3 | LD B3 |  | 
 |  | LD A4 | LD B4
 | Wait for Commit |  | 
 |  |  | Wait for Commit
A1, B1
A2, B2
A3, B3
A4, B4
SuppD |  |  |  |  | 
Issue | Issue | ROB1 | ROB2 | ROB3 | ROB4
LD A1 | LD B1 | LD A1 | LD B1 |  | 
LD A2 | LD B2 |  |  | LD A2 | LD B2
LD A3 | X |  | LD A3 |  | 
LD B3 | X |  |  |  | LD B3
X | X |  |  |  | 
LD A4 | X |  |  |  | LD A4
LD B4 | X | LD B4 |  |  | 
LD A5 | X |  |  | LD A5 | 
LD B5 | LD A6 | LD B5 | LD A6 |  | 
X | X |  |  |  | 
LD B6 | X | LD B6 |  |  | 
LD A7 | X |  |  |  | LD A7
LD B7 | X | LD B7 |  |  | 
LD A8 | X |  |  |  | 
B1
B2
B3
A1
A2
A3, B4
B5
B6
A5
A6, B7
Allow later instructions to commit before specific earlier instructions
  Problem: All instructions should commit in-order

## Slide 15: Terminal Load Optimization in DeSC
Allow later instructions to commit before specific earlier instructions
“Specific Instructions” = Terminal Loads which reached the head of ROB
  Terminal loads: loads where fetched value is only used for PRODUCE
    Compiler identifies & marks terminal loads (LOAD_PRODUCE instruction)
    Very common in decoupled archs, but non-existent in ordinary archs
SuppD Slice
SuppD Slice
Code before marking terminal loads
Code after marking terminal loads
for (i=0;i<N;i++)
{
idx = LOAD(&a[i])
tmp = LOAD(v&[idx])
PRODUCE(tmp)
}
for(i=0;i<N;i++)
{
idx = LOAD(&a[i])
LOAD_PRODUCE(&v[idx])
}

## Slide 16: Terminal Load Optimization in DeSC
When a terminal load reaches the head of a ROB, it is moved to the terminal load buffer if data is not ready
From terminal load buffer, it is moved to communication queue when data is ready
Property #1 : Any entry in terminal load buffer is non-speculative
  Terminal loads are only moved to buffer from the head of the ROB
Property #2 : No entry in terminal load buffer has dependents
  No need to update any other ROB entry with its load result
Reorder Buffer (ROB) |  | 
: : | : : | : :
Terminal Load Buffer (CAM) | 
ID | …
: : | 
If Data is not Ready
When Data is ready
Communication Queue
ID
DATA
Long Latency Terminal Load A
Short Latency Terminal Load B
Terminal Load A
If Data is ready
*B
*A
Data not ready
Data ready

## Slide 17: Terminal Load Optimization in DeSC
Terminal Load Optimization allows out-of-order insertion of data into communication queue
To support out-of-order data consumption, DeSC adds CAM Structure communication buffer
ID | Data
: : | : :
Comm. Buffer
(32-64 entries CAM)
Comm. Queue
(2-4KB FIFO)
ID
DATA
PRODUCE
CONSUME
Program order based ID is assigned for each PRODUCE & CONSUME so that CONSUME can find its matching counterpart
CONSUME

## Slide 18: Using general purpose OoO core as a SuppD
Simple microarch support
SuppD |  |  | 
ROB1 | ROB2 | ROB3 | ROB4
LD A1 | LD B1 |  | 
 |  | LD A2 | LD B2
 | Wait for LD A |  | 
 |  |  | Wait for LD A
LD A3 | LD B3 |  | 
 |  | LD A4 | LD B4
 | Wait for LD A |  | 
 |  |  | Wait for LD A
A1, B1
A2, B2
A3, B3
A4, B4
SuppD |  |  |  |  | 
Issue | Issue | ROB1 | ROB2 | ROB3 | ROB4
LD A1 | LD B1 | LD A1 | LD B1 |  | 
LD A2 | LD B2 |  |  | LD A2 | LD B2
LD A3 | X |  | LD A3 |  | 
LD B3 | X |  |  |  | LD B3
X | X |  |  |  | 
LD A4 | X |  |  |  | LD A4
LD B4 | X | LD B4 |  |  | 
LD A5 | X |  |  | LD A5 | 
LD B5 | LD A6 | LD B5 | LD A6 |  | 
X | X |  |  |  | 
LD B6 | X | LD B6 |  |  | 
LD A7 | X |  |  |  | LD A7
LD B7 | X | LD B7 |  |  | 
LD A8 | X |  |  |  | 
B1
B2
B3
A1
A2
A3, B4
B5
B6
A5
A6, B7
Better data supply throughput
DeSC terminal load optimization allows instruction to commit earlier than long latency terminal loads in specific cases

## Slide 19: DeSC Loss of Decoupling Optimizations
Supplier Side
Supplier Device (SuppD)
Computation Device (CompD)
Mem Interface
Communication Queue
Computation Side
PRODUCE
CONSUME
Loss of Decoupling (LOD) : SuppD cannot runahead because its data/control is dependent on CompD
Data Aliasing | Stall Reason
for(i=1;i<10;i++) { a[i] = a[i]*x v = a[5]*y } | 
a[5]’ =a[5]*x
a[5]’ = a[5] * x
a
[5]
Stall to wait for a[5] ‘= a[5]*x
a
[5]’
On 5th iteration, a[5] is updated in CompD so SuppD should stall until updated a[5] (= a[5] * x) to be passed from CompD
v = a’[5] * y
a[5]’
a[5]
*Comm. Buffer is not shown in the diagram for simplicity

## Slide 20: DeSC Loss of Decoupling Optimizations
Supplier Side
Supplier Device (SuppD)
Computation Device (CompD)
Mem Interface
Communication Queue
Computation Side
PRODUCE
Problem: SuppD stalls only to return the just received data back to CompD
Data Aliasing | DeSC Solution – Store to Load Forwarding
for(i=1;i<10;i++) { a[i] = a[i]*x v = a[5]*y } | 
a[5]’ =a[5]*x
a[5]’ = a[5] * x
a
[5]
  When SuppD needs to supply a value that will be computed in CompD, SuppD sends a pointer packet (pointing to the CompD’s temp buffer) instead of stalling.
  When consuming a pointer packet, CompD will re-use data from its own temporary buffer
SuppD inserts a pointer packet (pointing CompD’s temp buffer)
to the communication queue
Ptr
a[5]’
v = a’[5] * y
CONSUME
a[5]
Ptr
*Comm. Buffer is not shown in the diagram for simplicity
Allow CompD to hold recently computed values for a while and reuse them
Temporary buffer

## Slide 21: DeSC Performance Improvements
DeSC (OoO SuppD + OoO CompD) offers 2.04x average speedup over single core
  Overall speedup on par with perfect L1 cache
  Higher speedup on memory-bound workloads
  Terminal Load & LOD Optimizations are key to the speedup
*Mem-bound workloads use scaled axis on the right

## Slide 22: DeSC Performance Improvements
DeSC (OoO SuppD + Accelerator CompD) offers 1.56x speedup over accelerators with their own memory hierarchy
  DeSC provides better latency hiding ability than accelerators with its own memory hierarchy
Please check the paper for more evaluation results

## Slide 23: Conclusions
DeSC is a HW/SW framework which automatically manages and optimizes communication through decoupling
  Portability : Works with any given local storage size
  Performance : Minimizes latency exposed to computation
  Specialization : Communication and computation can use different devices
DeSC provides various optimizations
  Terminal load optimization
    Utilizes general purpose OoO core as the high-throughput data supplier
  Loss of decoupling optimization
    Allows supplier device to runahead without stalling for computation device
DeSC achieves 1.5x-2.0x speedup for different cases
Please check the paper for more details & explanations

## Slide 24: DeSC: Decoupled Supply-Compute Communication Management for Heterogeneous Architectures
Tae Jun Ham (Princeton Univ.)
Juan Luis Aragón (Univ. of Murcia) Margaret Martonosi (Princeton Univ.)
Paper URL : http://mrmgroup.cs.princeton.edu/papers/taejun_micro15.pdf

## Slide 25: More in Paper
Detailed DeSC hardware implementation
DeSC Compiler Pass implementation
More loss of decoupling optimizations
  More details on data aliasing LOD cases
  Computation dependent control optimization
  Computed address optimization
Evaluation methodologies
More evaluation results
  Only 2 out of 7 graphs are presented here
Detailed comparisons to the related works

## Slide 26: Backup : DeSC Hardware Diagram
STORE
ADDR
STORE
Cache, Memory Interface
Comm. Queue (FIFO Queue) |  | 
ID | Data | Fwd
: : | : : | : :
Value Computation
LOAD
STORE
VALUE
CONSUME
Comm. Buffer (CAM) |  | 
ID | Data | Fwd
: : | : : | : :
Register File
PRODUCE
LOAD_ PRODUCE
Terminal Load Buffer
Store Address Buffer (FIFO CAM) |  | 
Addr | Awt | Cnt
: : | : : | : :
LOAD_
PRODUCE
Addr
Store Value Buffer (FIFO Array) | 
Data | Cnt
: : | : :
CONSUME
Supplier Device (SuppD)
Computation Device (CompD)
Address Computation
Value