## Slide 1: Gather-Scatter DRAM In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses
Vivek Seshadri
Thomas Mullins, Amirali Boroumand, Onur Mutlu,
Phillip B. Gibbons, Michael A. Kozuch, Todd C. Mowry

## Slide 2: Executive summary
Problem: Non-unit strided accesses
  Present in many applications
  In-efficient in cache-line-optimized memory systems
Our Proposal: Gather-Scatter DRAM
  Gather/scatter values of strided access from multiple chips
  Ideal memory bandwidth/cache utilization for power-of-2 strides
  Requires very few changes to the DRAM module
Results
  In-memory databases: the best of both row store and column store
  Matrix multiplication: Eliminates software gather for SIMD optimizations

## Slide 3: Strided access pattern
Physical layout of the data structure (row store)
Record 1
Record 2
Record n
In-Memory Database Table
Field 1
Field 3

## Slide 4: Shortcomings of existing systems
Cache Line
Data unnecessarily transferred on the memory channel and stored in on-chip cache
High latency
Wasted bandwidth
Wasted cache space
High energy

## Slide 5: Prior approaches
Improving efficiency of fine-grained memory accesses
Impulse Memory Controller (HPCA 1999)
Adaptive/Dynamic Granularity Memory System (ISCA 2011/12)
Costly in a commodity system
Modules that support fine-grained memory accesses
  E.g., mini-rank, threaded-memory module
Sectored caches

## Slide 6: Goal: Eliminate inefficiency
Cache Line
Can we retrieve a only useful data?
Gather-Scatter DRAM
(Power-of-2 strides)

## Slide 7: DRAM modules have multiple chips
All chips within a “rank” operate in unison!
READ addr
Cache Line
?
Two Challenges!
Data
Cmd/Addr
Notes: Introduce the values .. Each chip provides 8 bytes.

## Slide 8: Challenge 1: Chip conflicts
Data of each cache line is spread across all the chips!
Cache line 0
Cache line 1
Useful data mapped to only two chips!

## Slide 9: Challenge 2: Shared address bus
All chips share the same address bus!
No flexibility for the memory controller to read different addresses from each chip!
One address bus for each chip is costly!
Notes: More pins from the processor to add address bus.

## Slide 10: Gather-Scatter DRAM
Column-ID-based data shuffling
(shuffle data of each cache line differently)
Pattern ID – In-DRAM address translation
(locally compute column address at each chip)
Challenge 1: Minimizing chip conflicts
Challenge 2: Shared address bus
Notes: Add “solution to challenge 1” etc.

## Slide 11: Column-ID-based data shuffling
Cache Line
Stage 1
Stage 2
Stage 3
Stage “n” enabled only if
nth LSB of column ID is set
DRAM Column Address
1
0
1
Chip 0
Chip 1
Chip 2
Chip 3
Chip 4
Chip 5
Chip 6
Chip 7
(implemented in the memory controller)

## Slide 12: Effect of data shuffling
Chip conflicts
Minimal chip conflicts!
Col 0
Col 1
Col 2
Col 3
Chip 0
Chip 1
Chip 2
Chip 3
Chip 4
Chip 5
Chip 6
Chip 7
Chip 0
Chip 1
Chip 2
Chip 3
Chip 4
Chip 5
Chip 6
Chip 7
Before shuffling
After shuffling
Can be retrieved in a single command

## Slide 13: Gather-Scatter DRAM
Column-ID-based data shuffling
(shuffle data of each cache line differently)
Pattern ID – In-DRAM address translation
(locally compute the column address at each chip)
Challenge 1: Minimizing chip conflicts
Challenge 2: Shared address bus

## Slide 14: Per-chip column translation logic
READ addr, pattern
cmd
addr
pattern
CTL
AND
pattern
chip ID
addr
cmd =
READ/WRITE
output address
XOR
Notes: Don’t send address – “locally compute the new address at each chip”
Ensure consistency in capitalization

## Slide 15: Gather-Scatter DRAM (GS-DRAM)
32 values contiguously stored in DRAM (at the start of a DRAM row)
read addr 0, pattern 0 (stride = 1, default operation)
read addr 0, pattern 1 (stride = 2)
read addr 0, pattern 3 (stride = 4)
read addr 0, pattern 7 (stride = 8)

## Slide 16: End-to-end system support for GS-DRAM
Memory controller
Cache Data Store
Tag
Store
Pattern ID
CPU
New instructions:
pattload/pattstore
GS-DRAM
miss
cacheline(addr), patt
DRAM column(addr), patt
pattload reg, addr, patt
Support for coherence of overlapping cache lines
Notes: Animation of a pattload execution

## Slide 17: Methodology
Simulator
  Gem5 x86 simulator
  Use “prefetch” instruction to implement pattern load
  Cache hierarchy
    32KB L1 D/I cache, 2MB shared L2 cache
  Main Memory: DDR3-1600, 1 channel, 1 rank, 8 banks
Energy evaluations
  McPAT + DRAMPower
Workloads
  In-memory databases
  Matrix multiplication

## Slide 18: In-memory databases
Layouts
Workloads
Row Store
Column Store
GS-DRAM
Transactions
Analytics
Hybrid
Notes: Tie it back non-unit strides
Background database

## Slide 19: Workload
Database
  1 table with million records
  Each record = 1 cache line
Transactions
  Operate on a random record
  Varying number of read-only/write-only/read-write fields
Analytics
  Sum of one/two columns
Hybrid
  Transactions thread: random records with 1 read-only, 1 write-only
  Analytics thread: sum of one column

## Slide 20: Transaction throughput and energy
Chart: 
| Transaction Throughput
Row Store | 24.24
Column Store | 8.55
GS-DRAM | 24.08
Chart: 
| Energy
Row Store | 16.99
Column Store | 49.65
GS-DRAM | 17.08
Throughput
(millions/second)
Energy
(mJ for 10000 trans.)
Row Store
GS-DRAM
Column Store
3X

## Slide 21: Analytics performance and energy
Row Store
GS-DRAM
Column Store
Chart: 
| Execution Time
Row Store | 2.07
Column Store | 0.86
GS-DRAM | 1.06
Chart: 
| Energy
Row Store | 95.44
Column Store | 40.32
GS-DRAM | 49.82
Execution Time (mSec)
Energy (mJ)
2X

## Slide 22: Hybrid Transactions/Analytical Processing
Chart: 
| Analytics
Row Store | 1.9225
Column Store | 0.605
GS-DRAM | 0.6625
Chart: 
| Transactions
Row Store | 19.68
Column Store | 16.62
GS-DRAM | 27.24
Execution Time (mSec)
Throughput
(millions/second)
Row Store
GS-DRAM
Column Store

## Slide 23: Conclusion
Problem: Non-unit strided accesses
  Present in many applications
  In-efficient in cache-line-optimized memory systems
Our Proposal: Gather-Scatter DRAM
  Gather/scatter values of strided access from multiple chips
  Ideal memory bandwidth/cache utilization for power-of-2 strides
  Low DRAM Cost: Logic to perform two bitwise operations per chip
Results
  In-memory databases: the best of both row store and column store
  Many more applications: scientific computation, key-value stores

## Slide 24: Gather-Scatter DRAM In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses
Vivek Seshadri
Thomas Mullins, Amirali Boroumand, Onur Mutlu,
Phillip B. Gibbons, Michael A. Kozuch, Todd C. Mowry

## Slide 25: Backup

## Slide 26: Maintaining Cache Coherence
Restrict each data structure to only two patterns
  Default pattern
  One additional strided pattern
Additional invalidations on read-exclusive requests
  Cache controller generates list of cache lines overlapping with modified cache line
  Invalidates all overlapping cache lines

## Slide 27: Hybrid Transactions/Analytical Processing
Chart: 
| w/o Pref. | Pref.
Row Store | 24.54 | 19.68
Column Store | 16.95 | 16.62
GS-DRAM | 27.4 | 27.24
Chart: 
| w/o Pref. | Pref.
Row Store | 10 | 1.9225
Column Store | 2.71 | 0.605
GS-DRAM | 2.73 | 0.6625
Execution Time (mSec)
Throughput
(millions/second)
Row Store
GS-DRAM
Column Store
21
Transactions
Analytics
Notes: Mark analytics and transactions on the slides

## Slide 28: Transactions Results
Chart: Execution time for 10000 trans.
| 1-0-1 | 2-1-2 | 0-2-2 | 2-4-2 | 5-0-1 | 2-0-4 | 6-1-2 | 4-2-2
Row Store | 1.56 | 1.56 | 1.65 | 1.65 | 1.66 | 1.74 | 1.66 | 1.74
Column Store | 2.43 | 3.29 | 4.28 | 6.08 | 6.03 | 6.2 | 6.91 | 7.99
GS-DRAM | 1.58 | 1.58 | 1.65 | 1.65 | 1.68 | 1.74 | 1.68 | 1.74