## Slide 1
GPU Register File Virtualization
Hyeran Jeon*¥, Gokul Subramanian Ravi€, Nam Sung Kim‡, and Murali Annavaram¥
University of Wisconsin-Madison€
University of Illinois, Urbana-Champaign‡
University of Southern California¥
San Jose State University*

## Slide 2
GPGPU became one of the most promising high performance computing engines
  It is everywhere (even in your laptop)
  It can run any program written in CUDA/OpenCL
  It outperforms CPU for data parallel tasks

## Slide 3
Chart: Register File Size (MB)
 | 1.9 | 2 | 3.8
GT200 Tesla (2008)
1.9MB Register File
GF110 Fermi (2010)
2MB Register File
768KB L2 shared cache
1.5MB L2 shared cache
GM200 Maxwell (2015)
4MB Register File
GK110 Kepler (2013)
3.8MB Register File

## Slide 4: Why GPGPU has such a large register file?
GPU
Register File
warp0
warp1
Context
switch
To enable frequent thread switching without
paying context switching penalty,
GPUs incorporate large register file.
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
t0
t1
t2
t31
. . .
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
t0
t1
t2
t31
. . .
Stack

## Slide 5: Why GPGPU has such a large register file?
GPU
Register File
warp0
warp1
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
t0
t1
t2
t31
. . .
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
t0
t1
t2
t31
. . .
To enable frequent thread switching without
paying context switching penalty,
GPUs incorporate large register file.

## Slide 6: Why GPGPU has such a large register file?
Register File
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
t0
t1
t2
t31
. . .
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
t0
t1
t2
t31
. . .
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
r0
r1
r2
..
r14
t0
t1
t2
t31
. . .
Warp 47
Warp 0
Warp 1
. . .
r0
r0
r0
r0
t0
t1
t2
t31
. . .
r14
r14
r14
r14
Register file in Fermi
can accommodate
48 warps per SM
(128KB RF per SM)
Large register file
Pros: Fast context switch
Cons: High power consumption
Register file is the most power hungry on-chip memory in GPGPU
Do we really need separate set of registers for each warp?

## Slide 7
Chart: Register file size reduction (%)
| 0 | 10 | 20 | 30 | 40 | 50
RF per-access power | 1 | 0.992 | 0.9639 | 0.9357 | 0.9076 | 0.8353
RF leakage power | 1 | 1.0202 | 0.9751 | 0.9221 | 0.8769 | 0.7461
Significant power reduction
only by shrinking the size
How do we get here?

## Slide 8: Register liveness
  Register liveness
    Live register: a register that contains a value that is consumed by following instruction(s)
    Dead register: a register that contains a value that is not consumed by following instruction (i.e. registers that are lastly read before next write in the code execution)
Ld r1, 0(r0)
Add r2, r1, r0
. . .
Sub r1, r3, r4
. . .
defined
used
re-defined
r1 is live
r1 is dead

## Slide 9: Not all registers are live all the time
  Fraction of live registers among compiler allocated registers is measured
  Significant fraction of registers are dead
   Exploit the underutilization to shrink register file size
LPS
backprop
hotspot
gaussian
< Fraction of live registers among compiler reserved registers captured during the execution >
(X-axis: cycle, Y-axis: utilization(%))

## Slide 10: Observations
THE REASON OF REGISTER SPACE UNDERUTILIZATION IN GPGPU

## Slide 11: Register activity patterns within a warp
3 representative register lifetime patterns are captured from an actual benchmark, matrixMul of CUDA SDK v3.0 (default compile options are used)
At compile time, none of the registers can be removed because they are concurrently alive, even though during very short time
Chart: 
time
(r3) Last Read before loop
(r0) Several Writes and Reads within a loop
(r2) Writes and immediate Reads within a loop and Reads after loop
(r3) Writes after loop
r3: Short lived
r2: Long lived
r0: Short lived but frequently accessed
Live
Dead
r3: dead

## Slide 12: Register space waste for short lived registers
Suppose single register in a warp is dead for a long time
What if there are N warps? (N can be several hundred in near future)
Due to warp scheduling (i.e. greedy, two-level), their lifetimes do not overlap
Chart: 
time
WarpN-R3
. . .
. . .
N registers
Warp3-R3
Warp2-R3
time
Warp1-R3
dead
Live
Dead

## Slide 13: Register space waste for short lived registers
Single short lived register usage in a kernel code causes hundreds of register space allocation in GPGPU
  Hundreds of dead registers burn power without any contribution to the program correctness
time
Chart: 
time
Warp1-R3
Warp2-R3
Warp3-R3
WarpN-R3
. . .
. . .
N registers
. . .
1 physical register
IDEA: Register Sharing
time
Live
Dead

## Slide 14: Register virtualization
EXPLOITING THE UNDERUTILIZED REGISTER SPACE FOR BETTER POWER EFFICIENCY

## Slide 15: Register file virtualization
Map large architected register file to smaller physical register file
  Register sharing across warps
  Register allocation minimization
Warp0 (r0, r1, r2 ..)
p0, p1, p2, …
Large architected register file
Smaller physical register file
Warp1 (r0, r1, r2 ..)
WarpN (r0, r1, r2 ..)
. . .

## Slide 16: How register file virtualization works?
Share register file across warps
Reallocate the dead register space for another warp’s register
A Register Bank
0
1
2
Pending Warp Queue
Ready Warp Queue
Execution
Units
write r3
2 Level Warp Scheduler
3
4
Sub-array
.
.
.
.
p0
p1
p2
p3
p4
p5
.
.
.
write register
Active
Register
Window
Warp0’s r3

## Slide 17: How register file virtualization works?
Share register file across warps
Reallocate the dead register space for another warp’s register
A Register Bank
1
0
2
Pending Warp Queue
Ready Warp Queue
Execution
Units
write r3
2 Level Warp Scheduler
3
4
.
.
.
.
p0
p1
p2
p3
p4
p5
.
.
.
write register
Active
Register
Window
Warp0’s r3
Warp1’s r3
Sub-array

## Slide 18: How register file virtualization works?
Share register file across warps
Reallocate the dead register space for another warp’s register
A Register Bank
0
1
2
Pending Warp Queue
Ready Warp Queue
Execution
Units
last read r3
2 Level Warp Scheduler
3
4
.
.
.
.
p0
p1
p2
p3
p4
p5
.
.
.
fetch register
Active
Register
Window
Warp0’s r3
Warp1’s r3
X
release
Sub-array

## Slide 19: How register file virtualization works?
0
1
2
Pending Warp Queue
Ready Warp Queue
Execution
Units
issue
2 Level Warp Scheduler
3
4
Cycles later…
warp 0 is stuck at
memory stall
 Schedule out
2
0
A Register Bank
.
.
.
.
p0
p1
p2
p3
p4
p5
.
.
.
Active
Register
Window
Warp1’s r3
Sub-array
Share register file across warps
Reallocate the dead register space for another warp’s register

## Slide 20: How register file virtualization works?
Share register file across warps
Reallocate the dead register space for another warp’s register
A Register Bank
2
1
3
Pending Warp Queue
Ready Warp Queue
Execution
Units
write r3
2 Level Warp Scheduler
4
0
.
.
.
.
p0
p1
p2
p3
p4
p5
.
.
.
write register
Active
Register
Window
Warp2’s r3
Warp1’s r3
Sub-array

## Slide 21: Compiler and Architectural support

## Slide 22: Where can registers be released?
Write A
Read A
.
.
Read A
Release A
.
.
Write A
Warps traverse diverged flows sequentially
Register release point needs to be carefully determined
Basic Block

## Slide 23: Where can registers be released?
Warps traverse diverged flows sequentially
Register release point needs to be carefully determined
Basic Block
Write A
Read A
❶
Read A
❷
Write A
Read A
❶
Read A
❷
Write A
Release A
Read A
❶
Read A
❷
Write A
Read A
❶
Read A
❷
Already released
Release A
Already released
Release A

## Slide 24: How to represent the release?
Compiler can embed release information into the kernel code
Option 1 ) Embed release information within each instruction
  Instruction format and decoding logic should be changed
Option 2 ) Add specialized release instructions (Our choice)
  Opcode of release instructions should be added
  We leverage existing metadata instruction decoding logic (details in paper)
0x80 .pir 001000...000010000
0x88 add $r4 $r5 $r0
... ...
0xE8 mov $r0 $r2
0xF0 shl $r4 $r0
0xF8 mad $r3 $r5 $r2 $r1
001 000 … 000 000 110
54-bit Release Flag
####
10-bit Per Instruction Release Flag OP code
- $r5 $r0
release
keep
######
010010 … 001100 000001
54-bit Release Flag
####
10-bit Per Branch
Release Flag OP code
######
reg1
reg9
< Per-Instruction Release instruction >
< Per-Branch Release instruction >

## Slide 25: How to release and rename registers?
❶ Warp 5 wants to read $r0
and the release flags are
 release $r0
w5: add $r3 $r0 $r2
PHYS. REG ID
. . .
P0
P8
P2
P5
. . .
Renaming Table
SM
SIMT Cluster 0
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
. . .
.
.
.
P1020
Occupied
Available
Register
Banks
SIMT Cluster 1
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
SIMT Cluster 7
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
1 0 1 1 1 1 . . . . 0
P0 1 2 3 4 5 . . . . 1023
Physical Register Availability Flag
P4
P4
P4
P0
P0
P0
0 1 0

## Slide 26: How to release and rename registers?
❷ After reading $r0 from $P0,
remove the mapping information
w5: add $r3 $r0 $r2
PHYS. REG ID
. . .
P0
P8
P2
P5
. . .
Renaming Table
SM
SIMT Cluster 0
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
. . .
.
.
.
P1020
Occupied
Available
Register
Banks
SIMT Cluster 1
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
SIMT Cluster 7
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
1 0 1 1 1 1 . . . . 0
P0 1 2 3 4 5 . . . . 1023
Physical Register Availability Flag
P4
P4
P4
P0
P0
P0
max # regs
per thread
X
+

## Slide 27: How to release and rename registers?
❷ After reading $r0 from $P0,
remove the mapping information
w5: add $r3 $r0 $r2
PHYS. REG ID
. . .
-
P8
P2
P5
. . .
Renaming Table
SM
SIMT Cluster 0
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
. . .
.
.
.
P1020
Occupied
Available
Register
Banks
SIMT Cluster 1
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
SIMT Cluster 7
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
0 0 1 1 1 1 . . . . 0
P0 1 2 3 4 5 . . . . 1023
Physical Register Availability Flag
P4
P4
P4
P0
P0
P0

## Slide 28: How to release and rename registers?
❸ When another warp (w3) wants
to write a new value to its register,
$P0 is remapped
w3: mov $r2 $r0
PHYS. REG ID
. . .
-
P8
P2
P5
. . .
Renaming Table
SM
SIMT Cluster 0
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
. . .
.
.
.
P1020
Occupied
Available
Register
Banks
SIMT Cluster 1
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
SIMT Cluster 7
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
0 0 1 1 1 1 . . . . 0
P0 1 2 3 4 5 . . . . 1023
Physical Register Availability Flag
P4
P4
P4
P0
P0
P0
$P0

## Slide 29: How to release and rename registers?
❸ When another warp (w3) wants
to write a new value to its register,
$P0 is remapped
w3: mov $r2 $r0
PHYS. REG ID
. . .
-
P8
P2
P5
. . .
Renaming Table
SM
SIMT Cluster 0
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
. . .
.
.
.
P1020
Occupied
Available
Register
Banks
SIMT Cluster 1
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
SIMT Cluster 7
.
.
.
P3
P7
P1023
.
.
.
P2
P6
P1022
.
.
.
P1
P5
P1021
.
.
.
P1020
1 0 1 1 1 1 . . . . 0
P0 1 2 3 4 5 . . . . 1023
Physical Register Availability Flag
P4
P4
P4
P0
P0
P0
$P0

## Slide 30
Physical register usage is cut by average of 16% due to register virtualization (Up to 44%)
  - ran optimally compiled applications (–maxrregcount compile option) on GPGPU-Sim v3.2.1
  - used PTXPlus simulation option to reflect realistic register allocation
Chart: Register Allocation Reduction (%)
| MatrixMul | BlackScho. | DCT8x8 | Reduction | VectorAdd | BackProp | BFS | Heartwall | HotSpot | LUD | Gaussian | LIB | LPS | NN | MUM | ScalarProd | AVG
 | 0.89286 | 18.75 | 38.0665 | 10.245 | 13.125 | 30.0781 | 13.8125 | 9.4971 | 15.9403 | 43.0198 | 40 | 3.7037 | 10.0658 | 8.5467 | 0.84978 | 6.6985 | 16.4557

## Slide 31
Chart: Register file size reduction (%)
| 0 | 10 | 20 | 30 | 40 | 50
RF per-access power | 1 | 0.992 | 0.9639 | 0.9357 | 0.9076 | 0.8353
RF leakage power | 1 | 1.0202 | 0.9751 | 0.9221 | 0.8769 | 0.7461
Now, can we get here?

## Slide 32
Chart: Physical register usage under register virtualization
| MatrixMul | BlackScho. | DCT8x8 | Reduction | VectorAdd | BackProp | BFS | Heartwall | HotSpot | LUD | Gaussian | LIB | LPS | NN | MUM | ScalarProd
 | 444 | 520 | 430.4375 | 315.9375 | 208.5 | 604.125 | 305.75 | 926.75 | 528 | 331.625 | 72 | 208 | 393.125 | 549.0625 | 904.25 | 806.125
Yes, for the applications that use no more than 64KB/SM registers under register reallocation
The other applications need some throttling method
to run on 50% smaller register file

## Slide 33: GPU-Shrink
WARP SCHEDULER FOR DEADLOCK AVOIDANCE

## Slide 34: GPU-Shrink Deadlock avoidance for register under-provisioning
With slight modification on warp scheduler, register file can be safely shrunk
Register File
warp0
warp1
CTA 0
warp0
warp1
CTA 1
r0, c1-w1
r1, c1-w1
r0, c0-w1
r1, c0-w1
r0, c1-w0
r1, c1-w0
r0, c0-w0
r1, c0-w0
Ex. 50% shrink
c0-w0
c0-w1
c1-w0
c1-w1
Each warp uses 2 registers, r0 and r1
Ready Queue

## Slide 35: GPU-Shrink Deadlock avoidance for register under-provisioning
With slight modification on warp scheduler, register file can be safely shrunk
Register File
r1, c0-w1
c0-w0
c0-w1
c1-w0
c1-w1
Ready Queue
Each warp uses 2 registers, r0 and r1
r0, c1-w1
r0, c0-w1
r0, c1-w0
r0, c0-w0
r1, c0-w0

## Slide 36: GPU-Shrink Deadlock avoidance for register under-provisioning
GPU-Shrink reserves a CTA-worth registers to guarantee at least one CTA can finish the execution without deadlock
c0-w0
c0-w1
c1-w0
c1-w1
Ready Queue
Register File
Each warp uses 2 registers, r0 and r1
available register count: 5
allocated registers for CTA0: 0
allocated registers for CTA1: 0
≥ a CTA register
demand (4 regs)
+

## Slide 37: GPU-Shrink Deadlock avoidance for register under-provisioning
c0-w0
c0-w1
c1-w0
c1-w1
Ready Queue
r0, c0-w0
Register File
GPU-Shrink reserves a CTA-worth registers to avoid deadlock
Each warp uses 2 registers, r0 and r1
available register count: 4
allocated registers for CTA0: 1
allocated registers for CTA1: 0
≥ a CTA register
demand (4 regs)
+

## Slide 38: GPU-Shrink Deadlock avoidance for register under-provisioning
c0-w0
c0-w1
c1-w0
c1-w1
Ready Queue
r0, c0-w0
r0, c0-w1
Register File
GPU-Shrink reserves a CTA-worth registers to avoid deadlock
Each warp uses 2 registers, r0 and r1
available register count: 3
allocated registers for CTA0: 2
allocated registers for CTA1: 0
≥ a CTA register
demand (4 regs)
+

## Slide 39: GPU-Shrink Deadlock avoidance for register under-provisioning
c0-w0
c0-w1
c1-w0
c1-w1
Ready Queue
r0, c0-w0
r0, c0-w1
r0, c1-w0
Register File
GPU-Shrink reserves a CTA-worth registers to avoid deadlock
Each warp uses 2 registers, r0 and r1
available register count: 2
allocated registers for CTA0: 2
allocated registers for CTA1: 1
≥ a CTA register
demand (4 regs)
+

## Slide 40: GPU-Shrink Deadlock avoidance for register under-provisioning
GPU-Shrink reserves a CTA-worth registers to avoid deadlock
c0-w0
c0-w1
c1-w0
c1-w1
Ready Queue
r0, c1-w1
Register File
Assign higher priority to CTA0
?


Each warp uses 2 registers, r0 and r1
CTA0 can’t finish execution with only 1 available register
Decline the request!
r0, c0-w0
r0, c0-w1
r0, c1-w0
available register count: 1?
allocated registers for CTA0: 2
allocated registers for CTA1: 2?
< a CTA register
demand (4 regs)
+
available register count: 2
allocated registers for CTA0: 2
allocated registers for CTA1: 1
≥ a CTA register
demand (4 regs)
+

## Slide 41: GPU-Shrink Deadlock avoidance for register under-provisioning
A CTA that uses the maximum # registers is assigned higher priority so that the CTA finishes the execution as early as possible
c0-w0
c0-w1
c1-w0
c1-w1
Ready Queue
r1, c0-w0
Register File
Assign higher priority to CTA0


Each warp uses 2 registers, r0 and r1
r0, c0-w0
r0, c0-w1
r0, c1-w0
available register count: 1
allocated registers for CTA0: 3
allocated registers for CTA1: 1
≥ a CTA register
demand (4 regs)
+

## Slide 42: GPU-Shrink Deadlock avoidance for register under-provisioning
A CTA that uses the maximum # registers is assigned higher priority so that the CTA finishes the execution as early as possible
c0-w0
c0-w1
c1-w0
c1-w1
Ready Queue
r1, c0-w0
r1, c0-w1
Register File
Assign higher priority to CTA0


Each warp uses 2 registers, r0 and r1
r0, c0-w0
r0, c0-w1
r0, c1-w0
available register count: 4
allocated registers for CTA0: 1
allocated registers for CTA1: 0
≥ a CTA register
demand (4 regs)
+

## Slide 43: GPU-Shrink Deadlock avoidance for register under-provisioning
The remaining CTAs resume their execution by using the released registers
c0-w0
c0-w1
c1-w0
c1-w1
Ready Queue
r0, c0-w0
r0, c0-w1
r0, c1-w0
r1, c0-w0
r1, c0-w1
Register File
Cycles later…
CTA0 finishes its execution
After warps in CTA0 release their registers,
warps in CTA1 can resume their execution
with the released registers.


Each warp uses 2 registers, r0 and r1
available register count: 4
allocated registers for CTA0: 1
allocated registers for CTA1: 0
≥ a CTA register
demand (4 regs)
+
available register count: 4
allocated registers for CTA1: 1
≥ a CTA register
demand (4 regs)
+

## Slide 44: Energy Saving
Register file virtualization + GPU-Shrink enables to safely shrink register file
50% smaller register file saves register file energy by 38%
Power gating escalates the energy saving to 42%
Chart: Total energy consumption normalized by 128KB RF
| 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | 128KB RF w/ PG | 64KB (50%) RF | 64KB (50%) RF w/ PG | MatrixMul | BlackScho. | DCT8x8 | Reduction | VectorAdd | BackProp | BFS | Heartwall | HotSpot | LUD | Gaussian | LIB | LPS | NN | MUM | ScalarProd | AVG
Static | 0.29988 | 0.32983 | 0.28765 | 0.29793 | 0.29935 | 0.31057 | 0.30568 | 0.31548 | 0.36213 | 0.2945 | 0.30094 | 0.29607 | 0.29909 | 0.30079 | 0.21668 | 0.3 | 0.30103
Dynamic | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832
Renaming Table | 0.00031378 | 0.0010423 | 0.0013224 | 0.00070864 | 1.7181e-06 | 0.00082473 | 0.00013063 | 4.2372e-05 | 0.00027528 | 6.8679e-05 | 0.00028529 | 0.00072385 | 0.00014489 | 9.8654e-05 | 0.00015669 | 0.00030899 | 0.00040306
Flag Instruction | 1.6996e-05 | 1.2267e-06 | 0.0036361 | 3.1478e-05 | 0.00093035 | 0.0036531 | 0.00010357 | 0.0085125 | 0.01533 | 0.0021167 | 9.9191e-07 | 7.7295e-05 | 0.021999 | 3.0794e-05 | 0.042964 | 0.0021678 | 0.0063482
Static | 0.28503 | 0.30844 | 0.15295 | 0.29752 | 0.14902 | 0.30719 | 0.15851 | 0.28609 | 0.27474 | 0.17913 | 0.15023 | 0.14803 | 0.2984 | 0.15317 | 0.21484 | 0.29837 | 0.22422
Dynamic | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832 | 0.34832
Renaming Table | 0.00031378 | 0.0010423 | 0.0013224 | 0.00070864 | 1.7181e-06 | 0.00082473 | 0.00013063 | 4.2372e-05 | 0.00027528 | 6.8679e-05 | 0.00028529 | 0.00072385 | 0.00014489 | 9.8654e-05 | 0.00015669 | 0.00030899 | 0.00040306
Flag Instruction | 1.6996e-05 | 1.2267e-06 | 0.0036361 | 3.1478e-05 | 0.00093035 | 0.0036531 | 0.00010357 | 0.0085125 | 0.01533 | 0.0021167 | 9.9191e-07 | 7.7295e-05 | 0.021999 | 3.0794e-05 | 0.042964 | 0.0021678 | 0.0063482
Static | 0.28503 | 0.46921 | 0.35514 | 0.30053 | 0.15045 | 0.45104 | 0.29839 | 0.55958 | 0.44778 | 0.17949 | 0.1505 | 0.1505 | 0.30026 | 0.15472 | 0.59408 | 0.58275 | 0.30179
Dynamic | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417 | 0.417
Renaming Table | 0.00031378 | 0.0010423 | 0.0013224 | 0.00070864 | 1.7181e-06 | 0.00082473 | 0.00013063 | 4.2372e-05 | 0.00027528 | 6.8679e-05 | 0.00028529 | 0.00072385 | 0.00014489 | 9.8654e-05 | 0.00015669 | 0.00030899 | 0.00040306
Flag Instruction | 1.6996e-05 | 1.2267e-06 | 0.0036361 | 3.1478e-05 | 0.00093035 | 0.0036531 | 0.00010357 | 0.0085125 | 0.01533 | 0.0021167 | 9.9191e-07 | 7.7295e-05 | 0.021999 | 3.0794e-05 | 0.042964 | 0.0021678 | 0.0063482
0.58

## Slide 45: Performance Impact
GPU-Shrink 50% derived almost 0% performance overhead on average
As a comparison, when applications are recompiled with 50% fewer registers, performance overhead was 73%
Chart: Execution cycle increase normalized by 128KB RF (%)
| MatrixMul | BlackScho. | DCT8x8 | Reduction | VectorAdd | BackProp | BFS | Heartwall | HotSpot | LUD | Gaussian | LIB | LPS | NN | MUM | ScalarProd | AVG
GPU-shrink | 0 | 1.6739 | -0.080659 | 0 | 0 | 16.2834 | -0.19576 | -2.0485 | 23.9723 | -0.01966 | 0 | 0 | 0 | -0.71453 | -29.5717 | 0 | 0.58117
Compiler spill | 13.8872 | 24.4365 | 110.8591 | 0 | 0 | 47.2334 | 0 | 33.2989 | 79.8517 | 28.9587 | 0 | 0 | 34.048 | 217.0065 | 1008.4246 | 323 | 73.322

## Slide 46: Summary
Inefficient register utilization is observed in massive parallel processor execution
Register virtualization allows warps to share physical registers thereby eliminating unnecessary register allocations
GPU-shrink allows an aggressive register file under-provisioning without any deadlock and performance overhead

## Slide 47: Thank you