## Slide 1: Border Control: Sandboxing Accelerators
Lena E. Olson, Jason Power, Mark D. Hill, David A. Wood
University of Wisconsin-Madison
MICRO-48 December 8th, 2015

## Slide 2: Executive Summary
Accelerators access shared host memory
  + Performance, programmability
  - Bugs, malicious design?
Protect host from accelerator wild reads/writes
Border Control
  provides full host memory safety (sandboxing)
  does not degrade performance
Performance overhead ~0.48%

## Slide 3: What is an accelerator?
Broadly:
Specialized hardware that can perform a
subset of computation tasks with
higher performance and/or lower energy
than a CPU.

## Slide 4: Accelerators are Pervasive
(GP)GPUs
ISPs
DSPs
Cryptographic
Neuromorphic
Approximate
Database
…..

## Slide 5: Accelerators are Programmable
HSA Model: host, accelerator share memory
Shared Physical Memory
  avoid copying data
Shared Virtual Memory
  pointer-is-a-pointer semantics
  improved programmability

## Slide 6: Untrusted Accelerators
May be designed by 3rd parties
May have bugs
  Even CPUs have bugs sometimes!
May be malicious
An incorrect accelerator with access to shared physical memory is a threat!

## Slide 7: Threat Model
Protect host from incorrect or malicious accelerators that could perform
stray reads, violating confidentiality
stray writes, violating integrity
of host processes that do and do NOT run on the accelerator

## Slide 8: Principle of Least Privilege
Every program and every user of the system should operate using the least set of privileges necessary to complete the job. Primarily, this principle limits the damage that can result from an accident or error.
Jerome Saltzer
hardware component
Border Control Authors

## Slide 9: Outline
Motivation
Current Systems
Border Control
Evaluation

## Slide 10: Direct Physical Address
CPU
$$
Trusted data path
Untrusted data path
$$
Memory or Shared LLC
MMU
TLB
Accel.
Address translation path
Translation update path
Accel.

## Slide 11: Full IOMMU
CPU
$$
Accel.
Trusted data path
Untrusted data path
$$
Memory or Shared LLC
Full IOMMU
MMU
TLB
Address translation path
Translation update path
Accel.

## Slide 12: Bypassable IOMMU (Baseline)
CPU
$$
Trusted data path
Untrusted data path
Memory or Shared LLC
$$
MMU
TLB
TLB
Accel.
$$
TLB
Accel.
$$
IOMMU
Address translation path
Translation update path
OS Memory (Q)
Process Memory (P)
Mem req:
Virtual addr = V
Mem req:
Phys. addr = P

## Slide 13: Bypassable IOMMU (Baseline)
CPU
$$
Trusted data path
Untrusted data path
Memory or Shared LLC
$$
MMU
TLB
TLB
Accel.
$$
TLB
Accel.
$$
IOMMU
Address translation path
Translation update path
OS Memory (Q)
Process Memory (P)
Mem req:
Phys. addr = P
Mem req:
Phys. addr = Q

## Slide 14: Outline
Motivation
Current Systems
Border Control
Evaluation

## Slide 15: Bypassable IOMMU (Baseline)
CPU
$$
Trusted data path
Untrusted data path
$$
MMU
TLB
TLB
Accel.
$$
TLB
Accel.
$$
IOMMU
Address translation path
Translation update path
Memory or Shared LLC
OS Memory (Q)
Process Memory (P)

## Slide 16: Border Control
CPU
$$
Trusted data path
Untrusted data path
$$
MMU
TLB
TLB
Accel.
$$
TLB
Accel.
$$
IOMMU
Address translation path
Translation update path
Memory or Shared LLC
OS Memory (Q)
Process Memory (P)
Border Control
Border Control

## Slide 17: Border Control
CPU
$$
Trusted data path
Untrusted data path
Memory or Shared LLC
$$
MMU
TLB
TLB
Accel.
$$
TLB
Accel.
$$
IOMMU
Address translation path
Translation update path
OS Memory (Q)
Process Memory (P)
Border Control
Border Control
Mem req:
Phys. addr = P
Mem req:
Virtual addr = V
Mem req:
Phys. addr = P

## Slide 18: Border Control
CPU
$$
Trusted data path
Untrusted data path
Memory or Shared LLC
$$
MMU
TLB
TLB
Accel.
$$
TLB
Accel.
$$
IOMMU
Address translation path
Translation update path
OS Memory (Q)
Process Memory (P)
Border Control
Border Control
Mem req:
Phys. addr = Q

## Slide 19: Border Control: Implementation
One Border Control instance per accelerator
Protection Table
  In system memory
  Contains all needed permissions by PPN
  Sufficient for correct design
  0.006% physical memory overhead
Border Control Cache (BCC)
  Caches recent permissions
  Each entry covers 512 4KB pages

## Slide 20: Protection Table Design
Flat physically indexed table in memory
2 bits (R/W) per physical page
  Initialized to 0 (no permission)
  Lazily updated on IOMMU translation
  Checked on all accelerator memory requests
●●●
PPN | R | W
0 | 0 | 0
1 | 1 | 1
2 | 1 | 0
3 | 0 | 0
N-4 | 0 | 0
N-3 | 1 | 0
N-2 | 1 | 0
N-1 | 0 | 0

## Slide 21: More details in paper!
Design of Border Control Cache
Actions: translation, page table updates, etc.
IBM CAPI
Multiprocess accelerators
Large pages
…..

## Slide 22: Outline
Motivation
Current Systems
Border Control
Evaluation

## Slide 23: Methodology
GPGPU  accelerator safety stress-test
Simulator: gem5-gpu
  Moderately-threaded: single core
  Highly-threaded: eight cores
Rodinia Benchmarks
Baseline: fast but unsafe bypassable IOMMU

## Slide 24: Border Control Overheads
Takeaway: Average 0.48% performance overhead
Moderately-Threaded GPU

## Slide 25: Border Control Overheads
Highly-Threaded GPU
Takeaway: Average 0.15% performance overhead

## Slide 26: Conclusion
Accelerators pose new security questions¹
Border Control provides full memory access protection / sandboxing
  with minimal impact on performance
  and low storage overhead
1. “Security Implications of Third-Party Accelerators” by Olson, Sethumadhavan, and Hill, CAL 2015

## Slide 27: Questions?

## Slide 28: IBM CAPI
CPU
$$
Trusted data path
Untrusted data path
Memory or Shared LLC
$$
MMU
TLB
TLB
Accel.
$$
TLB
Accel.
$$
IOMMU
Address translation path
Translation update path
OS Memory (Q)
Process Memory (P)

## Slide 29: TLB Shootdown Steps
If page was read-only:
  update entry in Protection Table and BCC
If page was read-write:
  Invalidate entry in TLB
  Flush dirty blocks from page in accelerator cache
  Update entry in Protection Table and BCC

## Slide 30: Simulation Parameters

## Slide 31: Comparison of Configurations

## Slide 32: Border Control Cache
Takeaway: A small (1KB) BCC is sufficient for our workloads

## Slide 33: Border Control Flush Overhead
Takeaway: Permission downgrades affect performance, but not much

## Slide 34: Information Flow Tracking
Goal: track untrusted information, prevent it from modifying sensitive data / control
  e.g., prevent buffer overflow in software
Hardware-assisted techniques: prevent threats from bugs in software (same address space) – different threat than Border Control
Hardware (e.g. Tiwari et al., ISCA 2011) – very powerful technique, but high area/runtime overhead and not transparent to software

## Slide 35: Mondriaan
Replacement for traditional page table + TLB
Allows fine-grained permissions
Border Control is independent of the policy for deciding permissions
  But permission granularity might mean alternate Protection Table organizations are better